HD CAR CAMERA

Key Definition Description

1.SD card slot                     2.the display                  3.emergency lock key          4.stand for position                 5.the speaker position          6.IR light

7.the lens                         8.the power button            9. the key

10.the menu button                 11.OK button

12. the mode button / long driveway offset by 5 seconds               13.the next key

14.Reset                         15.USB Interface

Power supply:

- Built-in battery-powered;

- USB power supply;

Features

Before using this product please insert TF card, all the files will be saved in the TF card;

- On / off function: Power: Press "power button" start;

Off: When turned on, press 3S "power button" Shutdown;

Other: Insert the car charger will automatically boot, unplug the car charger delay 10S automatic shutdown.

- Recording function: Press the MODE key to switch to video mode

Video: recording standby, short press "OK button" for video, short press the "OK button" to stop and save the video files;

- Camera functions: Press the Mode button to switch to camera mode

Photo: photo stand, short press "OK button" to take pictures;

- Playback functions: Press the Mode button to switch to playback mode

Playback: Playback mode, press the "key" or "under key" to select the file and press "OK button" to play the file;

5.  Plus / unlock functions:

Lock: when recording press the "lock key", the current recording video will lock protection;

Unlock: In playback mode to unlock through menu options;

- Lane deviation and collision warning before the car hit: the premise that the customer purchased the machine supports this feature, please click below if this feature to debug the machine reference

7.  The charging mode

When the access car charger, manual off into charging mode automatically, you need to press the "Power button" 3S to enter into video mode;

Video menu

Video mode, press the "Menu key" to enter the recording menu interface;

- The video format (video picture quality when shooting):

Set video resolution 1920 * 1080; 1440 * 1080; 1280 * 720; 640 * 480;

2. Head of the mark: on / off

3. Motion detection: Close / Open;

Off: When recording standby, DVR will not take any action;

Open: When recording standby, when the object moves in front of the camera to automatically turn on the video;

4. Loop recording time setting: 1 minute / 3 minutes / 5 minutes

When implementing segmented video recording time setting

5. Video sound: on / off

When the video input to achieve the sound on and off

6. The exposure value

When a positive bias brighter tone, while a negative tone dim

7. Lane departure warning / collision warning before the car

Achieve open and close the lane departure and before the car crash, but also to set the sensitivity level.

Camera menu

Camera mode press the "Menu key" into the camera menu interface;

The image size: 3M/5M/8M/10M

When negative effect dim, when positive, the effect of partial light;

Playback Menu

Deletion: Deletion leaflets or all

Lock / Unlock: Single or All

Thumbnail: achieve JiuGongTu Preview

Volume: The size of key tone and playing sound settings

System Menu

First click on the "menu button" click "Menu key" to enter the system menu interface;

1. Formatting; the entire contents inside TF card format

2. Language: Set for 12 languages ​​English / Chinese Simplified / Traditional Chinese / Korean Japanese / Russian / French / German / Spanish / Italian / Portuguese / Arabic

3. Automatic shutdown: within a set period of time without any operation after automatic shutdown time

Can be set to 1 minute 3 minutes 5 minutes on / off

4. Automatic off-screen: the screen saver time can be set from 1 minute 2 minutes 3 ​​minutes on / off

5. Reset the system: to restore factory settings

6. Power frequency: 50Hz/60Hz

7. The time set: Division conducted date set

8. USB Function: After setting plug the USB cable to connect the computer to the state of the removable disk / PC mode

9. Infrared light: Off / On / Auto

10. Version information: view the current system version;

Download file

- Connected to the computer USB, select "HDD" in the mode option;

- "Removable Disk" symbol appears on my computer;

- Download files DCIM folder;

Technical Parameters

| LCD screen size | 2.4-inch high-definition display |
| --- | --- |
| Maximum video resolution | FHD（1920*1080） |
| Video Format | AVI |
| Maximum resolution pictures | 10M |
| Photo Format | JPG |
| TF card | Support 4G-32G |
| Infrared night vision function | Support |
| Microphone / Speaker | Internal |
| Power Interface | 5VDC/1A |
| Battery | Built-in battery |

Note: This product retains the right to change design and specifications without notice any discrepancy, please prevail in kind.