BK215 Backhoe

Please Note

Make sure all potential operators of this equipment review this manual and all safety messages contained within.

This safety symbol indicates important safety messages in this manual. When you see this symbol, carefully read the message that follows and be alert to the possibility of personal injury or death.

CONTENTS

1. SAFETY PRECAUTIONS

2. SAFETY DECALS

3. BACKHOE SPECIFICATIONS

4. INTRODUCTION

5. TRACTOR PREPARATION

6. BACKHOE OPERATION

7. BACKHOE MOUNTING

8. BACKHOE REMOVAL

9. LUBRICATION AND MAINTENANCE

10. TROUBLE SHOOTING

11. HYDRAULIC SYSTEM SCHEMATIC

12. TORQUE TIGHTENING CHART

13. PART ILLUSTRATIONS

1. SAFETY PRECAUTIONS

SAFETY

Understand that your safety and the safety of other persons is measured by how you service and operate this Backhoe. Know the position and operations of all controls before you they to operate. Make sure you check all controls in all safe area before starting.

Read this manual completely and thoroughly and make sure you understand all controls. All equipment has a limit. Make sure you are aware of the stability and load characteristics of this Backhoe before you begin operation.

The safety information given in this manual does not replace any safety codes, insurance needs,  federal, state and local laws. Make sure your machine has the correct equipment required by your local laws and regulations.

CAUTION

This safety alert symbol indicates important safety messages in this manual. When you see this symbol, carefully read the message that follows and be alert to the possibility of personal injury or death.

SAFETY PRECAUTIONS

Before starting the engine of your tractor, make sure all operation controls are in park lock or neutral position.

Operate controls only when seated in the operator's seat.

Equip your tractor with a ROPS cab or frame for your protection. See your tractor operator's  manual for correct Seat belt usage.

A frequent cause of personal injury or death is persons falling off and being run over. Do not permit others to ride on your tractor. Only one person, the operator, should be on the machine when it is in operation.

Before leaving the tractor, stop the engine, put all controls in neutral, engage the parking brake and  remove the key from the ignition.

When using remote hydraulic tractor valves on some tractors, the Backhoe’s cylinders will  continue moving unless the control levers are manually returned to neutral, or until relief pressure is reached at the ends of piston strokes. Observe the bucket movement and maintain control with the control levers.

Stop the backhoe arms gradually when lowering or lifting loads. Stay off of slopes too steep for safe operation. Shift down before you start up or down a hill with a heavy load. Avoid "free wheeling".

Travel speed should be such that complete control and machine stability is maintained at all  times. Where possible, avoid operating operation near ditches, embankments and holes. Reduce  speed when turning, crossing slopes, and on rough, slick or muddy surfaces.

Never use your hand to check for suspected leaks under pressure. Use a piece of cardboard or  wood for this purpose. Escaping hydraulic oil or diesel fuel leaking under pressure can have sufficient force to penetrate the skin and cause infection or other injured by leaking fluid ,  seek medical attention immediately.

To prevent personal injury , relieve all pressure before disconnecting fluid lines.

Before applying hydraulic pressure, make sure all hydraulic connections are tight and components are in good condition.

Contact with overhead power lines can cause  severe electrical burn or death from electrocution.

Make sure there is enough clearance between raised equipment and overhead power lines.

Add recommended rear tire liquid weight or rear wheel weights for increased stability.

A backhoe attachment should be transported in a low position at slow ground speeds. Make turns slowly and use the tractor brakes cautiously. A loaded attachment in the raised position alters the center of gravity location of the machine and increases the possibility of mishaps.

Do not stand, walk or work under a raised backhoe or attachment unless it is securely blocked or held in position. Accidental movement of a control lever or leak in the hydraulic system could  cause the backhoe to drop, or attachment to dump, causing severe injury.

Make sure all parked backhoes on stands are on a hard level surface with all safety devices engaged to prevent backhoe from falling and being damaged or injuring someone.

When using a backhoe, be alert of bucket, boom and arm position at all times.

2. SAFETY DECALS

Safety Decal Locations

Important: Warning decals are visible when getting on backhoe.Refer to the left and right hands used in this manual, It's the position of the operator when seated in the operating position of backhoe.

Care of Safety Decals.

1. Keep safety decals clean and free of obstructing material.

2. Clean safety decals with soap and water and dry with a soft cloth.

3. Replace damaged or missing safety decals with new decals from your  Dealer.

4. If a component with a safety decal(s) affixed is replaced with a new part, make sure new safety decal(s) are attached in the same location(s) as the replaced components.

5. Mount new safety decals by applying on a clean dry surface and pressing air bubbles to outside edges.

Location : Mainframe                      Location : Both of Mainframe sides

Location : Both Leg Cylinders           Location : Both side of Mainframe

Location : Beside of the locking hole at the Boom Mainframe

Location : Main Valve Cover                   Location : Right Leg Guard

Location : Left side Valve Lever                Location : Right side Valve Lever

Location : Side of Left Inner Lever               Location : Side of Right Inner Lever

Location : Both side of Dipperstick             Location : Main Valve cover

3. BACKHOE SPECIFICATIONS

| Backhoe Model | BK215 |
| --- | --- |
| A | Digging Depth (two foot flat bottom) | 2200mm | 86.6” |
| B | Reach from center line of Swing Pivot | 3200mm | 126” |
| C | Loading Height(bucket at 60°) | 1850mm | 72.8” |
| D | Maximum Leveling Angle | 10° | 10° |
| E | Swing Arc | 180° | 180° |
| F | Transport Height (maximum) | 2120mm | 83.5” |
| G | Transport Overhang | 1230mm | 48.4” |
| H | Bucket Rotation | 180° | 180° |
| I | Stabilizer Spread (down position) | 1750mm | 68.9” |
| J | Stabilizer Spread (up position) | 1180mm | 46.5” |
| K | Angle of Departure | 21° | 21° |
|  | Shipping Weight (without bucket) | 415kg | 916(lbs) |
|  | Bucket Digging Force | 1175kg | 2592(lbs) |
|  | Dipperstick Digging Force | 895kg | 1975(lbs) |
|  | Operating Pressure | 160bar | 2320psi |

| Cylinder | Bore Diameter | Retracted Length | Stroke | Rod Diameter |
| --- | --- | --- | --- | --- |
|  | mm | inch | mm | inch | mm | inch | mm | inch |
| Boom | 70 | 2.75” | 620 | 24.41” | 384 | 15.12” | 40 | 1.57” |
| Bucket | 60 | 2.36” | 535 | 21.06” | 299 | 11.77” | 35 | 1.38” |
| Dipperstick | 60 | 2.36” | 597 | 23.5” | 377 | 14.84” | 35 | 1.38” |
| Swing | 60 | 2.36” | 398 | 15.67” | 223 | 8.78” | 35 | 1.38” |
| Stabilizer | 60 | 2.36” | 446 | 17.56” | 262 | 10.31” | 35 | 1.38” |

| Bucket | Teeth Q’ty | Struck Capacity | Heaped Capacity | Shipping Weight |
| --- | --- | --- | --- | --- |
| 12” | 3 | 1.01 cu.ft. | 1.24 cu.ft. | 35kg | 77(lbs) |

Specifications may vary depending on tractor model, tire size and bucket used.

4. INTRODUCTION

The purpose of this manual is to assist you in maintaining and operating your BK215 backhoe. Read it carefully, it furnishes information and instructions that will help you achieve years of dependable performance. Some information may be general in nature due to unknown and varying conditions. However, through experience and these instructions, you should be able to develop operating procedures suitable to your particular situation.

"Right" and "Left" as used throughout this manual are determined by facing the direction the machine will travel when in use.

The photos, illustrations and data used in this manual are current at the time of printing, but due to possible in-line production changes, your machine may vary slightly in detail. The manufacturer reserves the right to redesign the machine as may be necessary without notification.

Important:

Illustrations used in this manual may not show all safety equipment that is recommended to  ensure safe operation of tractor and backhoe. Refer to the Safety Precautions section of this  manual for information concerning safety. consult your dealer for further information.

Warranty Registration

The Delivery and Warranty Registration forms must be filled out and signed to validate your warranty protection. The items on the form under "I hereby Acknowledge" should be read and  understood. The terms and conditions of the warranty on this machine are specified in the front of this manual.

Serial Number and Location

The serial number is important information about the machine and it may be necessary to know it before obtaining the correct replacement part. The serial number is located on the right  side of backhoe mainframe. The serial number should be recorded on the Delivery and Registration form and also below for your reference.

5. TRACTOR PREPARATION

Rear Counterweight

CAUTION

Do not exceed the manufacturer's rating for maximum gross vehicle weight. Refer to Operator's Manual or ROPS serial plate provided with tractor. Certain specific conditions may not permit safe use of backhoe at backhoe rating or may require more careful restricted operation at the rated load.

ROPS System

The tractor must be equipped with an approved ROPS System to ensure adequate operator's protection.

Tractor Hydraulic System

Tractor operation in a backhoe application significantly increase demands on the tractor Hydraulic System. Check the tractor Hydraulic system fluid level daily. Refer to your tractor Operator's Manual maintenance section for instructions regarding tractor hydraulic system maintenance.

Adhere to recommendation in your Tractor Operator's Manual concerning hydraulic fluid and filter specifications, and change intervals.

CAUTION

The tractor/backhoe must only be operated with allsafety equipment properly installed.

Tire Inflation

Front tires must be maintained at the maximum recommend-ed inflation to maintain normal tire  profile with the added weight of backhoe/material.

Rear tires must be maintained at equal pressure within the recommended tire inflation range. Unequal rear tire inflation can prevent backhoe attachment from contacting the ground across its full width.

Wheel Tread Settings

Tractor front wheel tread setting must be restricted to wheel tread spacing recommended in the tractor Operator's Manual.

6. BACKHOE OPERATION

BACKHOE OPERATION

CAUTION

The tractor/backhoe should only be operated with all safety equipment properly installed. Keep assistants or by standers a safe distance from the equipment operating area.

Precautionary Notes

-Check below items before operating for your safety.

-Read and understand this manual to avoid accidents.

-Check the hydraulic fitting lines to be correct and set tightly.

-Maintain and repair (if it is needed) the parts or assemblies, check bolts and pins to be sure they are positioned tightly.

-Check tractor with the tractor operator's manual that it can prepared for operating.

-Warm up and operate the tractor and backhoe carefully. Purge any air in the hydraulic lines and cylinders by fully cycling all cylinders several times.

-Check hydraulic level in the tank. It should be full (Refer to the Tractor Operator's Manual).

-Do not operate the hydraulics when not seated in the back-hoe operator's seat.

-Keep all assistants out of area of operation.

-Do not operate rapidly.

-Do not allow riders other than the operator to be on the tractor while operating.

Important:

Use tractor engine speed that your experience permits. At first set PTO RPM of the tractor to slow.

Do not use the boom, dipperstick, swing and stabilizers to lift, push or full  objects. Use only  to maneuver and operate the bucket.

Important:

Practice quickly turning off the engine or stopping the backhoe immediately in case of an emergency situation.

Important:

Do not operate while the rear tractor wheels are off the ground by stabilizer. It is dangerous to operate the backhoe while rear wheels are off the ground.

Position vehicle so that the backhoe is as near to the pile as possible and in such a direction as to minimize the amount of tractor turning required to dump.

Keep the unit clean and perform regular service. Observe safety messages whenever cleaning, servicing, or lubricating.

We urge you to follow this advice:

1. Read and understand this manual as well the Tractor Operator's Manual.

2. Remember and observe the Safety Precautions brought to your attention in this manual, the tractor manual and on the machinery itself.

3. Use good common sense in the everyday operation of this unit. Safety recommendations can never be all-inclusive and you are responsible for watching out for and avoiding unsafe conditions.

4. Never exceed the limits of a piece of machinery. If its ability to do a job, or to do so safely, is in question, don't try it.

5. Don't hurry the learning process or take the unit for granted. Ease into it and become familiar with your new backhoe and tractor.

CAUTION

When lowering a heavy load, ease it downward slowly. Never drop a loaded attachment and "catch it hydraulically". Stopping a load after it has gained downward momentum places undue strain on the unit and may cause unnecessary damage to the backhoe or tractor or even worse, personal injury. Before disconnecting hydraulic lines, relieve all hydraulic pressure. Escaping hydraulic oil under pressure can have sufficient force to penetrate the skin causing serious personal injury. If injured by escaping hydraulic oil, seek medical attention immediately.

CAUTION

Do not operate the backhoe if the fittings are leaking or if the hoses are damaged. A sudden line burst would cause the boom, or dipperstick bucket to drop suddenly, causing damage to the tractor or backhoe or injury to personnel.

Initial Backhoe Operation

Before operating the backhoe, fully raise and lower the boom, arm, swing and stabilizers two or three times. Then raise the bucket above the ground and cycle the bucket cylinders three times.  Lower the bucket to the ground.

Check the tractor hydraulic oil and the correct oil level.

CAUTION

Before leaving the machine, stop the engine, remove the key, place all controls in neutral, and either set the parking brake or place tractor in park as equipped.

Always keep cylinders in a retracted position when the backhoe is not in use to guard against rust and contamination which may cause damage to the cylinder rods or hydraulic system. Also, lock the swing and boom while tractor is moving and storing for an extended period of time.

Cold Weather Operation

For smooth operation in cold weather, let the tractor warm up. Slowly cycle all of the cylinders several times to warm the oil in the hydraulic system. The backhoe may operate erratically until the hydraulic oil has warmed to operating temperatures.

CAUTION

Operate controls only when seated in the operator's seat.

Left and Right stabilizer controls

Left and Right Stabilizer controls

Push the left hand inner control lever, left stabilizer lowers. And pull up the lever, left stabilizer raises.

Push the right hand inner control lever, right stabilizer lowers. And pull up the lever, right stabilizer raises.

Do not dig near the stabilizers to avoid possible accident. Do not lift the tractor rear wheels by stabilizers.  Also, be sure the stabilizers are seated on hard ground to support. 
The backhoe/tractor.

Crowd and Swing controls

Push the left hand outer control lever, arm (dipperstick) moves toward the operator, and pull back the lever, arm (dipperstick) moves away from operator.

Move the left hand outer control lever to the left, boom swings moves to the left. Move lever right, boom swing moves to the Right.

Bucket and Boom controls

Push the right hand outer control lever, boom moves down, and pull back the lever, boom moves up.

Move the right hand outer control lever to the left, bucket curls in. Move lever right, bucket extends out from operator.

These two levers (Crowd and swing control lever, Bucket and Boom control lever) provide four  simultaneous operations. Both experience and practice are needed to eliminate excess motion and increase operating efficiency.

Swing Lock and Boom Lock When transporting or dismounting backhoe, you must lock the backhoe's swing and boom. Position boom straight back and drop pin through holes in swing frame and boom. When not in use, store pin in hole provided on swing frame and boom. Observe the following safety warnings when working with your new backhoe/tractor.

CAUTION

When using a backhoe, be aware of bucket and boom location at all times. When raising a arm (dipperstick) with bucket rolled forward, material can spill onto non target area causing injury to assistant or damage other objects. Do not dig near stabilizers. Ground under stabilizers could collapse. Make all movements slow and gradual when practicing operation. Operate from backhoe operators seat only. Pay attention, be ready to stop, immediately in case of an emergency. To help prevent roll-over, adjust the rear wheels to their widest setting to maximize stability. Refer to your Tractor Operator's Manual for recommendations.

7. BACKHOE MOUNTING

8. BACKHOE REMOVAL

BACKHOE REMOVAL

CAUTION

Move the backhoe to flat, firm and wide place to remove the equipment. Do not allow to be removed without bucket and stabilizers. Also, Dump the remaining material from the bucket to empty. Use other lifting equipment to remove when the backhoe has damage.

STEP 1. Move the tractor to backhoe storage place.

STEP 2. Use the inner two levers to lower the stabilizers until they contact to the ground. Use the boom and dipperstick control lever to raise the boom & dippers-tick completely.

STEP 3. Center the boom and then lock the swing with lock pin.

STEP 4. Using the control levers, position the dipperstick vertically, curl the bucket until its bottom is level with the ground, and lower the boom until bottom of the bucket rest on the ground.

STEP 5. Remove pins that secure the backhoe. Subframe in the mounting brackets on the tractor.

CAUTION

Remove the backhoe on firm level ground. Also, Do not allow the other person in the area. Be careful to avoid injury during removal of the backhoe. The hydraulic oil is dangerous for skin or eyes. Wash the skin and seek medical service if it is necessary.

STEP  6. Using both the stabilizer and boom control, set the backhoe subframe horizontally to relieve the weight of the backhoe from the mounting brackets of the tractor.

STEP  7. Move the tractor forward slowly until the backhoe subframe disengages of the mounting brackets.

STEP  8. Lower the backhoe mainframe to the ground by raising stabilizers and boom. Use the wood plate or block if necessary.

STEP  9. Turn off the tractor engine. Relieve hydraulic pressure by actuating all the control levers in each direction, then disconnect the backhoe hose couplers from the tractor hydraulic couplers.

9. LUBRICATION AND MAINTENANCE

LUBRICATION AND MAINTENANCE

| ITEM | SERVICE | SERVICE INTERVAL |
| --- | --- | --- |
| Hydraulic System Oil Level | Check | Daily/10 hours |
| Hydraulic System Oil/Filter | Replace | As specified in Tractor Operator's Manual |
| Tire Inflation | Check | Weekly/50 hours |
| Backhoe Pivot Points | Lubricate | Daily/10 hours |
| Backhoe Hydraulic Lines, Hoses, Connections | Check for leaks, wear | Daily/10 hours |
| Boom, Arm, Swing and Bucket cylinder rod packing | Check for seepage, service as needed | Daily/10 hours |
| Pivot pin bolts and dust covers | Check, replace if missing | Daily/10 hours |
| Friction of All pins | Check, replace if necessary | Daily/10 hours |
| Backhoe mount hardware | Check visually | Daily/10 hours |
| Bolts and Nut release | Re-torque | Every 25 hours |

CAUTION

Do not perform service or maintenance Operations with backhoe raised off the ground. For additional access to tractor components remove backhoe.

Important:

Lower the backhoe to the ground and relieve pressure in backhoe hydraulic lines prior to performing any service or maintenance operations on the tractor or backhoe.

CAUTION

Escaping fluid under pressure can have sufficient force to penetrate the skin , causing serious injury . Before disconnecting lines, be sure to relieve all pressure. Before applying pressure to the system, be sure all connections are tight and that lines, pipes and hoses are not damaged. Fluid escaping from a very small hole can be almost invisible. Use a piece of cardboard or wood rather than your hands to search for suspected leaks. If injured by escaping fluid, seek medical attention immediately. Serious infection or reaction can develop if correct medical treatment is not administered immediately.

Refer to "Lubrication and Maintenance Chart" for quick reference to Maintenance Operations.

CAUTION

Do not operate the backhoe if the fittings are leaking or if the hoses are damaged. A sudden line burst could cause the boom, dipperstick or bucket to drop suddenly, causing damage to the tractor or backhoe or injury to personnel. Operate the backhoe from the operator seat only. Do not stand or walk under a raised backhoe. Accidental movement of control lever or leak in hydraulic system could cause boom or dipperstick to drop, causing severe injury.

Check the tractor hydraulic system as outlined in the Tractor Operator's Manual.

NOTE

When checking hydraulic system oil level, the backhoe should be on the ground and bucket fully retracted(all cylinders in retracted position).

Grease all backhoe pivot points daily(10  hours). Refer to Tractor Operator's Manual for lubricant recommendations.

Inspect hydraulic hoses, connections, control valve and cylinders for evidence of leakage.

Tractor tires should be maintained at maximum recommended inflation to maintain normal tire profile with added weight of backhoe/material. Unequal rear tire inflation can result in bucket not being level to the ground.

10. TROUBLE SHOOTING

TROUBLE SHOOTING

This Trouble Shooting Chart is provided for reference to possible backhoe operational problems. Determine the problem that best describes the operational problem being experienced and eliminate the possible causes as listed by following the correction procedures.

| PROBLEM | POSSIBLE CAUSE | CORRECTION |
| --- | --- | --- |
| Swing, Boom, Dipperstick and Bucket Cylinders Not operating properly | Low hydraulic fluid level. | Check and replenish hydraulic fluid. |
|  | Hydraulic hoses connected improperly | Check and correct hydraulic hose connections |
|  | Hydraulic hoses to/from control valve blocked | Check for damage (kinked) hoses, etc |
|  | Backhoe control valve or tractor main relief valve stuck open | Check system pressure. Repair or replace relief valve. Refer to the Tractor Operator's Manual |
|  | Low system pressure supplied from hydraulic pump | Check system pressure. Repair or replace pump |
|  | Control valve linkage broken | Inspect. Repair as required |
|  | Quick disconnect coupler(s) are not fully connected or "Flow Check" | Check coupler connections. Replace coupler(s) if necessary |
|  | Hydraulic hose or tube line blockage | Check for evidence of damage to hoses or tube lines that would block flow of oil between cylinders and control valve |
|  | Cylinder piston assembly defective (not sealing) | Check cylinders for internal leakage as described in service section under cylinder leakage tests. |
|  | Control valve blockage | Inspect for blockage. Disassemble valve if necessary. |
| Cylinders operate in wrong direction relative to control valve lever position | Hydraulic hoses connected incorrectly | Correct hydraulic hose connections |

| Slow or erratic movement of Cylinders (Noisy operation of cylinders) | Low hydraulic fluid level. | Check and replenish hydraulic fluid |
| --- | --- | --- |
|  | Cold hydraulic fluid | Allow hydraulic system to warm up to operating temperature |
|  | Hydraulic Oil viscosity too heavy or Incorrect oil | Check oil number and viscosity, Refill correct hydraulic oil |
|  | Engine R.P.M. too slow (hydraulic pump R.P.M. too slow) | Increase engine speed to obtain satisfactory backhoe operation |
|  | Excessive weight in bucket. Material weight exceeds maximum specified backhoe capacity | Reduce material load. (Digging load) |
|  | Control valve linkage binding/defective | Check control valve linkage and repair if worn/defective. |
|  | Aeration of hydraulic fluid | Refer to "Aeration of Hydraulic Fluid" |
|  | Quick disconnect coupler restriction or coupler "Flow checks" | Check coupler connections. Repair or replace |
|  | Hydraulic hose or tube line restriction (hoses/tube line) kinked or pinched | Check hoses and tube lines for evidence of restriction |
|  | Boom, Dipperstick or Bucket cylinder piston assembly leakage | Check cylinders for leakage. Repair as needed |
|  | Relief valve erratic or set below specifications | Check and reset relief valve. Setting as needed. |
|  | Control valve leaking internally.(hypassing fluid within valve). | Replace control valve and recheck operation. |
| Inadequate lifting capacity | Engine R.P.M. too slow. | Increase engine R.P.M |
|  | Excessive load. Material loading exceeds specified backhoe capacity | Reduce Load |
|  | Relief valve setting below specifications | Check and reset relief valve setting as needed. |
|  | Bucket, Boom and Dipperstick cylinder piston assembly leakage | Check cylinders for leakage. Repair as needed |
|  | Control valve leaking internally | Replace control valve and recheck operation |
|  | Hydraulic pump defective | Refer to "Hydraulic Pump Capacity Inadequate". |
| Aeration of Hydraulic Fluid(Generally indicated by foamy appearance of fluid) | Low hydraulic fluid level | Check and refill hydraulic system to proper level. |
|  | Air leaking into suction side of hydraulic pump. | Check for loose or defective connections between reservoir and hydraulic pump |
|  | Hydraulic fluid foaming due to improper hydraulic oil usage | Refer to Tractor Operator's Manual and replace hydraulic oil using recommended hydraulic oil. |

| System relief valve squeals. | Cold Hydraulic Fluid | Allow hydraulic fluid to warm up to operating temperature |
| --- | --- | --- |
|  | Hydraulic Oil viscosity too heavy or Incorrect oil | Check oil number and viscosity, Refill correct hydraulic oil. |
|  | Excessive load in bucket. Loading exceeds specified backhoe capacity | Reduce load |
|  | Relief valve setting below specifications | Check and reset valve setting as needed |
|  | Hydraulic hose, tube line or quick disconnect coupler restriction | Check for evidence of restriction in hydraulic oil flow. Repair or replace defective components |
| Backhoe drops with valve spool in "centered" position (no external oil leakage evident) Note: A gradual drop over an extended period of time is a normal condition. | Cylinder piston assembly leakage | Check cylinders for leakage |
|  | Control valve internal leakage | Replace control valve and recheck |
| Control valve spool(s) will not return to centered position | Control lever linkage binding | Determine origin of binding and repair |
|  | Control valve spool centering is broken | Replace centering spring |
|  | Control valve spool binding in valve body spool bore | Disassemble valve for inspection and repair. |
| External hydraulic fluid leakage | Loose hydraulic connection | Tighten loose connections |
|  | Defective hydraulic hose, tube line, adapter fitting or adapter fitting o-ring | Check for origin of oil leak and replace defective part. |
|  | Control valve o-rings defective | Replace defective o-rings |
|  | Control valve spool or body damaged or worn | Replace control valve |
|  | Cylinder rod packing set leakage | Check cylinders for leakage. Repair as needed |
| Hydraulic pump capacity inadequate | Cold hydraulic fluid | Allow hydraulic fluid to warm up to operating temperature |
|  | Engine R.P.M. too slow | Increase engine R.P.M |
|  | Low hydraulic fluid supply | Refer to Tractor Operator's Manual for service recommendations |
|  | Hydraulic hose restriction | Check for evidence of restriction in hydraulic hoses |
|  | Hydraulic pump defective | Refer to Tractor Operator's Manual for recommended service procedures. Replace hydraulic pump if determined to be defective |
| Cylinder rod bend when cylinders extended | Excessive shock load on cylinders during transport | Replace defective parts. Review and observe proper and safe operational practices |

11. HYDRAULIC SYSTEM SCHEMATIC

HYDRAULIC SYSTEM SCHEMATIC AUXILIARY HYDRAULIC VALVE PACKAGE

12. TORQUE TIGHTENING CHART

TORQUE TIGHTENING CHART 1

TORQUE TIGHTENING CHART 2

13. PART ILLUSTRATIONS

| BK215-00-001 Excavator Assembly |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Quantity |
| 1 | BK215-04-001 | Control console Assembly | 操作台总成 | 1 |
| 2 | BK215-08-001 | Arm-brace Assembly(Right) | 撑脚总成-右 | 1 |
| 3 | BK215-03-001 | Big arm Assembly | 大臂总成 | 1 |
| 4 | BK215-02-001 | Small arm Assembly | 小臂总成 | 1 |
| 5 | BK215-01-001 | Bucket Assembly | 挖斗总成 | 1 |
| 6 | BK215-09-001 | The swing seat Assembly | 摆座总成 | 1 |
| 7 | BK215-10-001 | Base Assembly | 底座总成 | 1 |
| 8 | BK215-08-002 | Arm-brace Assembly(Left) | 撑脚总成-左 | 1 |
| 9 | BK215-06-001 | Seat Assembly | 座椅总成 | 1 |

| BK215-01-001 Bucket Assembly |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Qty | Remarks |
| 1 | GB/T1152-M6 | Oil cup | 油杯M6 | 4 |  |
| 2 | BK215-01-012 | Inner plate welding | 内连接板焊合 | 1 |  |
| 3 | JDB253340 | Axle sleeve φ25×φ33×40 | 轴套φ25×φ33×40 | 2 |  |
| 4 | GB/T 889.1-M8 | Locking nut M8 | 防松螺母M8 | 2 |  |
| 5 | GB/T5782-M8x55 | Bolt M8x55 | 螺栓M8x55 | 2 |  |
| 6 | BK215-01-101 | Bucket pin | 挖斗销 | 2 |  |
| 7 | BK215-01-011 | 12 inch Bucket welding | 12寸挖斗焊合 | 1 | 12 inch（Standard） |
|  | BK215-01-011A | 14 inch Bucket welding | 14寸挖斗焊合 | 1 | 14 inch（selection） |
|  | BK215-01-011B | 16 inch Bucket welding | 16寸挖斗焊合 | 1 | 16 inch（selection） |
| 8 | BK215-01-102 | Bucket shovel tooth | 挖斗铲齿 | 3 |  |
| 9 | GB/T 889.1-M12 | Locking nut M12 | 防松螺母M12 | 6 |  |
| 10 | GB/T5782-M12x45 | Bolt M12x45 | 螺栓M12x45 | 6 | 10.9 class |

| BK215-02-001 Small arm Assembly |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Qty |
| 1 | BK215-07-011 | Bucket cylinder | 挖斗油缸 | 1 |
| 2 | BK215-02-102 | Upper pin of connecting plate | 连接板上销 | 1 |
| 3 | BK215-02-103 | Lower pin of connecting plate | 连接板下销 | 1 |
| 4 | GB/T1152 | Oil cup | 油杯M6 | 2 |
| 5 | BK215-02-012 | The outer connecting plate(Left) | 外连接板焊合（左） | 1 |
| 6 | JDB253340 | Axle sleeve φ25×φ33×40 | 轴套φ25×φ33×40 | 2 |
| 7 | JDB303840 | Axle sleeve φ30×φ38×40 | 轴套φ30×φ38×40 | 2 |
| 8 | BK215-02-013 | The outer connecting plate(Right) | 外连接板焊合（右） | 1 |
| 9 | GB/T 889.1-M8 | Locking nut M8 | 防松螺母M8 | 4 |
| 10 | GB/T 5782-M8x60 | Bolt M8x60 | 螺栓 M8×60 | 4 |
| 11 | BK215-02-101 | Small arms Pin | 小臂销 | 2 |
| 12 | JDB405040 | Axle sleeve φ40×φ50×40 | 轴套φ40×φ50×40 | 2 |
| 13 | BK215-02-011 | Small arm welding | 小臂焊合 | 1 |

| BK215-03-001 Big arm Assembly |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Qty |
| 1 | BK215-07-013 | Lifting cylinder | 提升油缸 | 1 |
| 2 | BK215-07-012 | Extension cylinder | 伸展油缸 | 1 |
| 3 | BK215-03-011 | The big arm welding | 大臂焊合 | 1 |
| 4 | GB/T5782-M8x70 | Bolt M8x70 | 螺栓M8x70 | 2 |
| 5 | GB/T 889.1-M8 | Locking nut M8 | 防松螺母M8 | 3 |
| 6 | BK215-03-102 | Big arm pin | 大臂销 | 2 |
| 7 | BK215-03-101 | Large arm cylinder pin | 大臂油缸销 | 1 |
| 8 | GB/T 5782-M8x60 | Bolt M8x60 | 螺栓 M8×60 | 1 |

| BK215-04-001 Control console Assembly |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Qty | Remarks |
| 1 |  | Rubber dust cover 84×84 | 橡胶防尘套 84×84 | 2 |  |
| 2 | BK215-04-102 | Control console | 操作台 | 1 | Domestic valve |
|  | BK215-04-102A | Control console | 操作台 | 1 | Imported valve |
| 3 | GB/T 5783-M8×20 | Bolt M8×20 | 螺栓 M8×20 | 18 |  |
| 4 | GB/T 93-8 | Spring washer 8 | 弹垫 8 | 8 |  |
| 5 | GB/T 97.1-8 | Plain washers 8 | 平垫 8 | 36 |  |
| 6 | BK215-04-011 | Welded seat | 阀座焊合 | 1 | Domestic valve |
|  | BK215-04-011A | Welded seat | 阀座焊合 | 1 | Imported valve |
| 7 | GB/T 889.1-M12 | Locking nut M12 | 防松螺母M12 | 8 |  |
| 8 | GB/T 97.1-12 | Plain washers 12 | 平垫 12 | 8 |  |
| 9 | GB/T 5783-M12×40 | Bolt M12×40 | 螺栓 M12×40 | 8 |  |
| 10 | BK215-04-012 | Tie rod fixing seat | 拉杆固定座 | 1 |  |
| 11 | BK215-04-107 | Pull rod rubber sleeve | 拉杆橡胶套 | 1 |  |
| 12 | BK215-04-013 | Pull rod | 拉杆 | 1 |  |
| 13 | BK215-04-104 | Foot board(Left) | 脚踏板-左 | 1 |  |
| 14 | BK215-04-105 | Foot board(Right) | 脚踏板-右 | 1 |  |
| 15 | GB/T 889.1-M8 | Locking nut M8 | 防松螺母M8 | 14 |  |
| 16 | BK215-04-106 | Foot board(Middle) | 中间脚踏板 | 1 | Standard |
|  | BK215-04-106A | Foot board(Middle) | 中间脚踏板 | 1 | with tank（selection） |
| 17 | GB/T5783-M8×35 | Bolt M8×35 | 螺栓M8×35 | 4 |  |
| 18 | BK215-04-103 | Hand pipe | 手扶管 | 1 |  |
| 19 | BK215-04-101 | The front cover of Control console | 操作台前盖 | 1 |  |

| BK215-06-001 Seat Assembly |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Qty |
| 1 | BK215-06-102 | Cushion Assembly | 坐垫总成 | 1 |
| 2 | GB/T70.1 | Hexagon socket head cap screws M8x20 | 内六角圆柱头螺钉 M8x20 | 4 |
| 3 | GB/T 97.1 | Plain washers 8 | 平垫 8 | 4 |
| 4 | GB/T 889.1 | Locking nut M8 | 防松螺母M8 | 4 |
| 5 | BK215-06-012 | Support welding | 座椅支座焊合 | 1 |
| 6 | BK215-06-101 | cross-pin | 插销 | 1 |
| 7 | DIN11024 | R Pin φ3.2 | R销 φ3.2 | 1 |
| 8 | BK215-06-013 | The Seat connecting plate welding | 座椅连接板焊合 | 1 |
| 9 | GB/T 889.1 | Locking nut M12 | 防松螺母M12 | 2 |
| 10 | GB/T5782 | Bolt M12×110 | 螺栓 M12x110 | 1 |
| 11 | GB/T5782 | Bolt M12×100 | 螺栓 M12x100 | 1 |
| 12 | BK215-06-011 | The seat support pipe welding | 座椅撑管焊合 | 1 |
| 13 | GB/T 5783 | Bolt M12×40 | 螺栓 M12×40 | 6 |
| 14 | GB/T 93 | Spring washers 12 | 弹垫 12 | 6 |
| 15 | GB/T 97.1 | Plain washers 12 | 平垫 12 | 6 |

| BK215-07-001 Hydraulic system ( with tank) |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Qty | Remarks |
| 1 | DL39-E15L-T | Multiway valve | 多路阀 | 1 |  |
| 2 | GB/T3452.1 | O ring 13（O.D ）x1.9 | O型圈 13（外径）x1.9 | 5 | matched with joint |
| 3 | BK215-07-103 | M22x1.5-M18x1.5 | M22x1.5-M18x1.5 | 2 |  |
| 4 | GB/T3452.1 | O ring 19.3（I.D ）x2.4 | O型圈 19.3(内径)x2.4 | 2 | matched with joint |
| 5 | BK215-07-026 | Inlet pipe of valve | 阀进油管 | 1 |  |
| 6 | BK215-10-017 | Hydraulic tank assembly | 液压油箱装配 | 1 |  |
| 7 | GB/T3452.1 | O ring 20（I.D ）x2.3 | O型圈 20（外径）x2.3 | 12 | matched with joint |
| 8 | BK215-07-101 | M20X1.5-M14X1.5 | M20X1.5-M14X1.5 | 8 |  |
| 9 | BK215-07-017 | Lifting cylinder tubing | 提升油缸油管 | 2 |  |
| 10 | GB/T3452.1 | O ring 10（I.D ）x1.9 | O型圈 10（外径）x1.9 | 32 | matched with joint |
| 11 | JB/T966 | M14X1.5-M14X1.5 | M14X1.5-M14X1.5 | 16 | 1EL-14-14 |
| 12 | JB/T982 | Composite gasket 14 | 组合垫 14 | 16 |  |
| 13 | BK215-07-018 | Bucket Cylinder front tubing | 挖斗油缸前段油管 | 2 |  |
| 14 | JB/T966 | Over plate joint M14x1.5-M14x1.5 | 过板接头M14x1.5-M14x1.5 | 2 | With nut |
| 15 | BK215-07-022 | Bucket cylinder rear section pipe | 挖斗油缸后段油管 | 2 |  |
| 16 | BK215-07-019 | Foot cylinder tubing | 撑脚油缸油管 | 4 |  |
| 17 | BK215-07-020 | swinging cylinder oil pipe | 偏摆油缸油管 | 2 |  |
| 18 | BK215-07-023 | swinging cylinder Connecting tubing | 偏摆油缸连接油管 | 2 |  |
| 19 | BK215-07-102 | M20X1.5-M14X1.5 Small hole | M20X1.5-M14X1.5小孔 | 4 |  |
| 20 | BK215-07-021 | Extension cylinder oil pipe | 伸展油缸油管 | 2 |  |
| 21 | BK215-07-013 | Lifting cylinder | 提升油缸 | 1 |  |
| 22 | BK215-07-011 | Bucket cylinder | 挖斗油缸 | 1 |  |
| 23 | BK215-07-015 | Foot cylinder（R） | 撑脚油缸-右 | 1 |  |
| 24 | BK215-07-016 | Foot cylinder(L) | 撑脚油缸-左 | 1 |  |
| 25 | BK215-07-014 | swinging cylinder | 偏摆油缸 | 2 |  |
| 26 | BK215-07-012 | Extension cylinder | 伸展油缸 | 1 |  |
| 27 | GB/T5782 | Bolt M10x70 | 螺栓M10x70 | 2 |  |
| 28 | GB/T889.1 | Locking nut M10 | 防松螺母M10 | 2 |  |
| 29 | GB/T5785 | Bolt M10x1.25x60 | 螺栓M10x1.25x60 | 1 |  |
| 30 | BK215-07-025 | Valve return pipe | 阀回油管 | 1 |  |
| 31 | 700M-18 | Hollow bolt M18x1.5 | 空芯螺栓 M18x1.5 | 1 |  |
| 32 | ZHD-18 | Composite gasket M18x1.5 | 组合垫 M18x1.5 | 2 |  |
| 33 | CBW-310 | Oil pump transmission box | 油泵传动箱 | 1 |  |
| 34 | GB/T3452.1 | O ring 22x2.5 | O型圈 22x2.5 | 2 |  |
| 35 | BK215-10-111 | Oil pump flange joint | 油泵法兰接头 | 2 |  |
| 36 | BK215-07-027 | Gear pump inlet pipe | 齿轮泵进油管 | 1 |  |
| 37 | 04B-600 | Transmission shaft | 传动轴 | 1 |  |

| BK215-07-001 Hydraulic system |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Qty | Remarks |
| 1 | DL39-E15L-T | Multiway valve | 多路阀 | 1 |  |
| 2 | GB/T3452.1 | O ring 13（O.D ）x1.9 | O型圈 13（外径）x1.9 | 2 | matched with joint |
| 3 | BK215-07-103 | M22x1.5-M18x1.5 | M22x1.5-M18x1.5 | 2 |  |
| 4 | GB/T3452.1 | O ring 19.3（I.D ）x2.4 | O型圈 19.3(内径)x2.4 | 2 | matched with joint |
| 5 | BK215-07-024 | Inlet-outlet-tube | 进出油管 | 2 |  |
| 6 | ISO7241-1B | Quick change joint | 快换接头R1/2" | 2 |  |
| 7 | GB/T3452.1 | O ring 20（I.D ）x2.3 | O型圈 20（外径）x2.3 | 12 | matched with joint |
| 8 | BK215-07-101 | M20X1.5-M14X1.5 | M20X1.5-M14X1.5 | 8 |  |
| 9 | BK215-07-017 | Lifting cylinder tubing | 提升油缸油管 | 2 |  |
| 10 | GB/T3452.1 | O ring 10（I.D ）x1.9 | O型圈 10（外径）x1.9 | 32 | matched with joint |
| 11 | JB/T966 | M14X1.5-M14X1.5 | M14X1.5-M14X1.5 | 16 | 1EL-14-14 |
| 12 | JB/T982 | Composite gasket 14 | 组合垫 14 | 16 |  |
| 13 | BK215-07-018 | Bucket Cylinder front tubing | 挖斗油缸前段油管 | 2 |  |
| 14 | JB/T966 | Over plate joint M14x1.5-M14x1.5 | 过板接头M14x1.5-M14x1.5 | 2 | With nut |
| 15 | BK215-07-022 | Bucket cylinder rear section pipe | 挖斗油缸后段油管 | 2 |  |
| 16 | BK215-07-019 | Foot cylinder tubing | 撑脚油缸油管 | 4 |  |
| 17 | BK215-07-020 | swinging cylinder oil pipe | 偏摆油缸油管 | 2 |  |
| 18 | BK215-07-023 | swinging cylinder Connecting tubing | 偏摆油缸连接油管 | 2 |  |
| 19 | BK215-07-102 | M20X1.5-M14X1.5 Small hole | M20X1.5-M14X1.5小孔 | 4 |  |
| 20 | BK215-07-021 | Extension cylinder oil pipe | 伸展油缸油管 | 2 |  |
| 21 | BK215-07-013 | Lifting cylinder | 提升油缸 | 1 |  |
| 22 | BK215-07-011 | Bucket cylinder | 挖斗油缸 | 1 |  |
| 23 | BK215-07-015 | Foot cylinder（R） | 撑脚油缸-右 | 1 |  |
| 24 | BK215-07-016 | Foot cylinder(L) | 撑脚油缸-左 | 1 |  |
| 25 | BK215-07-014 | swinging cylinder | 偏摆油缸 | 2 |  |
| 26 | BK215-07-012 | Extension cylinder | 伸展油缸 | 1 |  |
| 27 | GB/T5782 | Bolt M10x70 | 螺栓M10x70 | 2 |  |
| 28 | GB/T889.1 | Locking nut M10 | 防松螺母M10 | 2 |  |
| 29 | GB/T5785 | Bolt M10x1.25x60 | 螺栓M10x1.25x60 | 1 |  |

| BK215-07-001 Hydraulic system ( with Imported valve) |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Qty | Remarks |
| 1 | TR55 | Imported Multiway valve | 进口多路阀 | 1 |  |
| 2 | GB/T3452.1 | O ring 13（O.D ）x1.9 | O型圈 13（外径）x1.9 | 2 | matched with joint |
| 3 | 1EG-18-06 | Transition joint G3/8 turn M18x1.5 (O) | 过渡接头G3/8转M18x1.5（O） | 2 |  |
| 4 | ZHD-18 | Composite gasket 18 | 组合垫18 | 14 | matched with joint |
| 5 | BK215-07-024 | Inlet-outlet-tube | 进出油管 | 2 |  |
| 6 | ISO7241-1B | Quick change joint | 快换接头R1/2" | 2 |  |
| 8 | BK215-07-101A | Transition joint G3/8-M14x1.5 | 过渡接头G3/8-M14x1.5 | 8 |  |
| 9 | BK215-07-017 | Lifting cylinder tubing | 提升油缸油管 | 2 |  |
| 10 | GB/T3452.1 | O ring 10（I.D ）x1.9 | O型圈 10（外径）x1.9 | 32 | matched with joint |
| 11 | JB/T966 | M14X1.5-M14X1.5 | M14X1.5-M14X1.5 | 16 | 1EL-14-14 |
| 12 | JB/T982 | Composite gasket 14 | 组合垫 14 | 16 |  |
| 13 | BK215-07-018 | Bucket Cylinder front tubing | 挖斗油缸前段油管 | 2 |  |
| 14 | JB/T966 | Over plate joint M14x1.5-M14x1.5 | 过板接头M14x1.5-M14x1.5 | 2 | With nut |
| 15 | BK215-07-022 | Bucket cylinder rear section pipe | 挖斗油缸后段油管 | 2 |  |
| 16 | BK215-07-019 | Foot cylinder tubing | 撑脚油缸油管 | 4 |  |
| 17 | BK215-07-020 | swinging cylinder oil pipe | 偏摆油缸油管 | 2 |  |
| 18 | BK215-07-023 | swinging cylinder Connecting tubing | 偏摆油缸连接油管 | 2 |  |
| 19 | BK215-07-102A | Transition joint G3/8-M14X1.5 small hole | 过渡接头G3/8-M14X1.5小孔 | 4 |  |
| 20 | BK215-07-021 | Extension cylinder oil pipe | 伸展油缸油管 | 2 |  |
| 21 | BK215-07-013 | Lifting cylinder | 提升油缸 | 1 |  |
| 22 | BK215-07-011 | Bucket cylinder | 挖斗油缸 | 1 |  |
| 23 | BK215-07-015 | Foot cylinder（R） | 撑脚油缸-右 | 1 |  |
| 24 | BK215-07-016 | Foot cylinder(L) | 撑脚油缸-左 | 1 |  |
| 25 | BK215-07-014 | swinging cylinder | 偏摆油缸 | 2 |  |
| 26 | BK215-07-012 | Extension cylinder | 伸展油缸 | 1 |  |
| 27 | GB/T5782 | Bolt M8x100 | 螺栓M8x100 | 2 |  |
| 28 | GB/T889.1 | Locking nut M8 | 防松螺母M8 | 2 |  |
| 29 | GB/T5785 | Bolt M8x45 | 螺栓M8x45 | 1 |  |

| BK215-08-001 Arm-brace Assembly (Right) |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Qty |
| 1 | BK215-07-015 | Arm-brace cylinder(Right) | 撑脚油缸（右） | 1 |
| 2 | BK215-08-011 | Arm-brace cylinder Welding(Right) | 撑脚焊合（右） | 1 |
| 3 | BK215-08-101 | Arm-brace cylinder Cylinder pin | 撑脚油缸销一 | 1 |
| 4 | BK215-08-102 | Plate pin | 撑板销 | 1 |
| 5 | GB/T 889.1-M8 | Locking nut M8 | 防松螺母M8 | 2 |
| 6 | GB/T 5782-M8×50 | Bolt M8×50 | 螺栓 M8×50 | 2 |
| 7 | BK215-08-013 | Support plate Welding | 撑板焊合 | 1 |
| 8 | GB/T1152-M6 | Oil cup | 油杯M6 | 2 |

| BK215-08-002 Arm-brace Assembly(Left) |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Qty |
| 1 | BK215-07-016 | Arm-brace cylinder(Left) | 撑脚油缸（左） | 1 |
| 2 | BK215-08-012 | Arm-brace cylinder Welding(Left) | 撑脚焊合（左） | 1 |
| 3 | GB/T1152-M6 | Oil cup | 油杯M6 | 2 |
| 4 | BK215-08-013 | Support plate Welding | 撑板焊合 | 1 |
| 5 | BK215-08-101 | Arm-brace cylinder Cylinder pin | 撑脚油缸销一 | 1 |
| 6 | GB/T 889.1-M8 | Locking nut M8 | 防松螺母M8 | 2 |
| 7 | GB/T 5782-M8×50 | Bolt M8×50 | 螺栓 M8×50 | 2 |
| 8 | BK215-08-102 | Plate pin | 撑板销 | 1 |

| BK215-09-001 The swing seat Assembly |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Qty |
| 1 | JB/T7271.3-M10×32 | Handle sleeve M10×32 | 手柄套 M10×32 | 1 |
| 2 | BK215-09-013 | handle welding | 锁架手柄焊合 | 1 |
| 3 | GB/T 5783-M8×25 | Bolt M8×25 | 螺栓 M8×25 | 1 |
| 4 | GB/T 889.1-M8 | Locking nut M8 | 防松螺母 M8 | 6 |
| 5 | BK215-09-012 | Lock frame welding | 锁架焊合 | 1 |
| 6 | GB 894.2-22 | Circlips for shaft 22 | 轴用弹性挡圈 22 | 2 |
| 7 | BK215-09-101 | Lock pin | 锁架销 | 1 |
| 8 | GB/T1152-M6 | Oil cup | 油杯M6 | 3 |
| 9 | BK215-09-102 | Swing seat pin | 摆座销 | 2 |
| 10 | GB/T5782- M8×70 | Bolt M8×70 | 螺栓M8×70 | 2 |
| 11 | JDB405040 | Axle sleeve φ40×φ50×40 | 轴套φ40×φ50×40 | 2 |
| 12 | BK215-09-103 | Oscillating cylinder pin | 摆动油缸销 | 2 |
| 13 | BK215-09-011 | The swing seat welding | 摆座焊合 | 1 |
| 14 | BK215-02-101 | Small Arm pin | 小臂销 | 1 |
| 15 | GB/T 5782-M8×60 | Bolt M8×60 | 螺栓 M8×60 | 1 |
| 16 | GB/T 889.1-M10 | Locking nut M10 | 防松螺母M10 | 1 |
| 17 | GB/T 97.1-10 | Plain washers 10 | 平垫 10 | 1 |
| 18 | GB/T 5783-M10×35 | Bolt M10×35 | 螺栓 M10×35 | 1 |
| 19 | BK215-09-105 | Drag spring | 拉簧 | 1 |
| 20 | BK215-09-104 | Lock frame hinge plate | 锁架铰链板 | 1 |
| 21 | GB/T5782-M8×55 | Bolt M8×55 | 螺栓M8×55 | 2 |

| BK215-10-017 Hydraulic tank assembly |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Qty |
| 1 | QUQ1 | Hydraulic air filter | 液压空气滤清器 | 1 |
| 2 | GB/T 5783-M8×20 | Bolt M8×20 | 螺栓 M8×20 | 8 |
| 3 | GB/T 93-8 | Spring lock washers 8 | 弹垫 8 | 8 |
| 4 | GB/T 97.1-8 | Plain washers 8 | 平垫 8 | 8 |
| 5 | DK2000-111 | Sealed flange | 密封法兰盘 | 1 |
| 6 | DK2000-113 | Paper pad | 纸垫 | 1 |
| 7 | BK215-10-018 | The tank body welding | 油箱体焊合件 | 1 |
| 8 | GB/T 889.1-M10 | Locking nut M10 | 防松螺母M10 | 4 |
| 9 | GB/T 97.1-10 | Plain washers 10 | 平垫 10 | 8 |
| 10 | GB/T 5783-M10×40 | Bolt M10×40 | 螺栓 M10×40 | 4 |
| 11 | WU-16x80-J | Hydraulic oil filter | 液压油滤清器 | 1 |
| 12 | ZHD-18 | compound gasket M18x1.5 | 组合垫 M18x1.5 | 2 |
| 13 | 6.00E-18 | Over plate joint M18x1.5（O） | 过板接头M18x1.5（O） | 1 |

| BK215-10-001 Base assembly |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Qty | Remarks |
| 1 | GB/T5782 | Bolt M16x65 | 螺栓 M16x65 | 4 |  |
| 2 | GB/T 97.1 | Plain washers 16 | 平垫 16 | 4 |  |
| 3 | GB/T 889.1 | Locking nut M16 | 防松螺母 M16 | 4 |  |
| 4 | GB/T 6170 | nut M8 | 螺母 M8 | 4 | 8 class |
| 5 | BK215-10-106 | U shape hoop | U形抱箍 | 1 |  |
| 6 | GB/T1152 | Oil cup M6 | 油杯M6 | 4 |  |
| 7 | BK215-10-013 | Swing cylinder seat | 摆动油缸座 | 1 |  |
| 8 | BK215-07-014 | Tilting cylinder | 偏摆油缸 | 2 |  |
| 9 | GB/T 5782 | Bolt M22x120 | 螺栓 M22×120 | 6 |  |
| 10 | GB/T 97.1 | Plain washers 22 | 平垫 22 | 12 |  |
| 11 | GB/T889.1 | Locking nut M22 | 防松螺母M22 | 6 |  |
| 12 | LS-22T-107 | Lower suspension pin (with chain) | 下悬挂销（带链条） | 2 |  |
| 13 | BK215-10-109 | Lower suspension outer panel | 下悬挂外板 | 2 |  |
| 14 | BK215-10-108 | Suspension support sleeve | 悬挂支撑套 | 6 |  |
| 15 | BK215-10-011 | Welding base | 底座焊合 | 1 |  |
| 16 | BK215-10-019 | The limit rod welding | 限位杆焊合 | 1 |  |
| 17 |  | 40 round rubber jacket | 40圆橡胶外套 | 2 |  |
| 18 | JFB4030 | RCB-JFB Φ40×Φ50×30 | 带翻边轴套Φ40×Φ50×30 | 2 |  |
| 19 | BK215-10-107 | The swing seat Washers | 摆座垫圈 | 4 |  |
| 20 | GB/T 5782 | Bolt M8x50 | 螺栓 M8×50 | 4 |  |
| 21 | GB/T 889.1 | Locking nut M8 | 防松螺母M8 | 6 |  |
| 22 | BK215-08-102 | Plate pin | 撑板销 | 2 |  |
| 23 | BK215-10-104 | Foot cylinder pin 2 | 撑脚油缸销二 | 2 |  |
| 24 | BK215-10-101 | Foot fixing plate | 撑脚固定板 | 2 |  |
| 25 | BK215-10-012 | Resist collision Seat | 摆座防撞座 | 2 |  |
| 26 | BK215-10-103 | Resist collision Rubber block | 摆座防撞橡胶块 | 2 |  |
| 27 | GB/T5782 | Bolt M10x100 | 螺栓M10x100 | 2 |  |
| 28 | GB/T 97.1 | Plain washers 10 | 平垫 10 | 4 |  |
| 29 | GB/T 889.1 | Locking nut M10 | 防松螺母M10 | 4 |  |
| 30 | BK215-10-102 | The pressure spring | 压簧 | 2 |  |
| 31 | GB/T5782 | Bolt M10x50 | 螺栓M10x50 | 2 |  |
| 32 | EFGC175.116 | Upper suspension pin | 上悬挂销 | 1 |  |
| 33 | GB/T 4329 | Lock pin 12 | 锁销 12 | 1 |  |
| 34 | BK215-10-105 | Brace rubber pad | 撑脚橡胶垫 | 2 |  |

| BK215-10-001 Base assembly with tank ( selection) |
| --- |
| Ser.No. | Part No. | Name & Specification |  | Qty | Remarks |
| 1 | GB/T5782-M10×100 | Bolt M10×100 | 螺栓M10×100 | 2 |  |
| 2 | GB/T 97.1-10 | Plain washers 10 | 平垫 10 | 8 |  |
| 3 | GB/T 889.1-M10 | Locking nut M10 | 防松螺母M10 | 4 |  |
| 4 | BK215-10-103 | Resist collision Rubber block | 摆座防撞橡胶块 | 2 |  |
| 5 | BK215-10-012 | Resist collision Seat | 摆座防撞座 | 2 |  |
| 6 | BK215-08-102 | Plate pin | 撑板销 | 2 |  |
| 7 | GB/T5782-M10×50 | Bolt M10×50 | 螺栓M10×50 | 2 |  |
| 8 | BK215-10-101 | Foot fixing plate | 撑脚固定板 | 2 |  |
| 9 | BK215-10-102 | The pressure spring | 压簧 | 2 |  |
| 10 | BK215-10-104 | Foot cylinder pin 2 | 撑脚油缸销二 | 2 |  |
| 11 | GB/T 889.1-M8 | Locking nut M8 | 防松螺母M8 | 6 |  |
| 12 | GB/T 5782-M8×50 | Bolt M8×50 | 螺栓 M8×50 | 4 |  |
| 13 | BK215-10-107 | The swing seat Washers | 摆座垫圈 | 4 |  |
| 14 | JFB4030-Φ40×Φ50×30 | RCB-JFB Φ40×Φ50×30 | 带翻边轴套Φ40×Φ50×30 | 2 |  |
| 15 | BK215-10-011 | Welding base | 底座焊合 | 1 |  |
| 16 | GB/T5783-M12×45 | Bolt M12×45 | 螺栓 M12×45 | 4 |  |
| 17 | GB/T 97.1-12 | Plain washers 12 | 平垫 12 | 16 |  |
| 18 | GB/T 889.1-M12 | Locking nut M12 | 防松螺母M12 | 8 |  |
| 19 | BK215-10-110 | Upper connecting plate | 上连接板 | 2 |  |
| 20 | BK215-10-017 | Hydraulic tank assembly | 液压油箱装配 | 1 |  |
| 21 | GB/T 4329-12 | Lock pin 12 | 锁销 12 | 1 |  |
| 22 | EFGC175.116 | Upper suspension pin | 上悬挂销 | 1 |  |
| 23 | BK215-10-016 | Column | 立柱 | 1 |  |
| 24 | GB/T 5783-M12×50 | Bolt M12×50 | 螺栓 M12×50 | 4 |  |
| 25 | GB/T 5783-M22×65 | Bolt M22×65 | 螺栓 M22×65 | 8 |  |
| 26 | GB/T 97.1-22 | Plain washers 22 | 平垫 22 | 16 |  |
| 27 | GB/T889.1-M22 | Locking nut M22 | 防松螺母M22 | 8 |  |
| 28 | LS-22T-107 | Lower suspension pin (with chain) | 下悬挂销（带链条） | 2 |  |
| 29 | BK215-10-014 | Right lower suspension bracket | 右下悬挂支架 | 1 |  |
| 30 |  | 40 round rubber jacket | 40圆橡胶外套 | 2 |  |
| 31 | BK215-10-019A | The limit rod welding | 限位杆焊合 | 1 | with tank (selection) |
| 32 | BK215-10-015 | Left lower suspension bracket | 左下悬挂支架 | 1 |  |
| 33 | BK215-07-014 | Tilting cylinder | 偏摆油缸 | 2 |  |
| 34 | CBW-310 | Oil pump transmission box | 油泵传动箱 | 1 |  |
| 35 | BK215-10-013 | Swing cylinder seat | 摆动油缸座 | 1 |  |
| 36 | GB/T1152-M6 | Oil cup M6 | 油杯M6 | 4 |  |
| 37 | GB/T 6170-M8 | nut M8 | 螺母 M8 | 4 |  |
| 38 | BK215-10-106 | U shape hoop | U形抱箍 | 1 |  |
| 39 | GB/T5782-M16×65 | Bolt M16×65 | 螺栓 M16×65 | 4 |  |
| 40 | GB/T 97.1-16 | Plain washers 16 | 平垫 16 | 4 |  |
| 41 | GB/T 5783-M10×25 | Bolt M10×25 | 螺栓 M10×25 | 4 |  |
| 42 | GB/T 889.1-M16 | Locking nut M16 | 防松螺母 M16 | 4 |  |
| 43 | GB/T 93-10 | Spring lock washers 10 | 弹垫 10 | 4 |  |
| 44 | BK215-10-105 | Brace rubber pad | 撑脚橡胶垫 | 2 |  |