Instructions of Sawdust Briquette Machine

1.  Use and Characters

This machine is used to compress biomass materials with lignin, such as sawdust, rice husk, peanut shells, agro wastes, etc., into solid briquette.

The briquette machine uses the temperature control display may in establish under the temperature the stable operation, and has the structure to be reasonable, operation service simple and so on merits. The solid briquettes which produced by sawdust briquette machine catches fire, the calorific value high, when combustion the contamination are few, the proportion is bigger than storing and the transportation.

2.  Working Principle

Using the lignin raw material intrinsic property, through the screw extrusion, under the high temperature, the high pressure, in the lignin raw material’s lignin plasticizing causes the tiny textile fiber to unify, forms the clavate solid fuel.

- Raw Material’s Condition

  - Moisture Content 8-12%

  - Granularity ≤6mm

- Briquette Features

  - External Diameter -50-90mm, internal diameter-taylored, Length- taylored

  - Density- 1200-1300kg/m3

  - Heating Value 4000-5500Kcal/kg

- Structure Drawing

- Installation and Commissioning

  - Fastening all screws and bolts, and connecting power.

  - Inspection all oil site to check whether has input oil, especially in gearbox(replace gearbox oil every 4-5 months).

  - To check supply voltage whether is normal.

  - Start machine to run 5 minutes with un-loading, to make sure the briquette machine has no noise and other abnormal condition, then input raw materials evenly. Please stop the machine when testing has any problems, like noise. After checking and solving the problems, and then commissioning the machines with no-loading again.

  - Settle the temperature modulator reaching requested 400’C, when the temperature achieves the temperature, and then start the machine with raw materials feeding evenly.

  - Increase raw materials feeding gradually, until producing certified briquettes. It indicates the briquette machine commissioning successfully when produced regular briquettes 30 minutes.

  - The hopper must be no raw materials before stop briquette machine. And reverse the machine 1 minute to guarantee raw materials in screw propeller back.

  - The supply power must connect ground wire.

- Faults & Solutions

| No. | Faults |  | Causes |  |  | Solutions |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | a. | Not connect | supply | a. | Check supply power |
| 1 | Indicator light is not light |  | power |  | b. | Replace indicator light |
|  |  | b. | Indicator | light |  |  |

|  |  |  | breakdown |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | a. | Control button damage | a. | Replace |  | control |
|  |  | b. | Only | 2 | phases working |  | button |  |  |  |
| 2 | Motor doesn’t work |  | not 3 phases |  |  | b. | Check supply power |
|  |  | c. | Voltage | or | frequency | c. | Inspect | voltage | and |
|  |  |  | doesn’t suitable |  |  | frequency |  |  |
|  | The heating temperature | a. | The | supply | voltage is | a. | Inspect voltage |  |
|  |  |  | low |  |  |  |  | b. | Replace | the | heating |
| 3 | rises slowly or cannot |  |  |  |  |  |  |  |  |  |  |
|  |  | b. | The |  | heating | ring |  | rings |  |  |  |
|  | reach 350’C |  |  |  |  |  |  |  |  |  |  |
|  |  |  | breakdown |  |  |  |  |  |  |  |
|  |  | a. | The loading is too much | a. | Inspect |  | switch, |
|  | Problems of motor | b. | The working condition is |  | contacts, and phases |
| 4 |  |  | higher |  |  |  | b. | Clear motor’s clutters |
|  | heating |  |  |  |  |  |  |  |
|  |  | c. | Voltage is too low or |  | around motor |  |  |
|  |  |  | high |  |  |  |  | c. | Adjust supply voltage |
|  |  | a. | Raw | materials moisture | a. | Dry raw | materials to |
|  |  |  | content is higher |  |  | control | moisture | is |
|  |  | b. | The |  |  |  | heating |  | 8-12% |  |  |  |
|  |  |  | temperature |  | is | b. | Rises the | heating |
| 5 | Cannot make briquettes |  | low-don’t reach 400’C |  | temperature | reach |
|  |  | c. | The voltage is too low |  | 400’C+ |  |  |  |
|  |  | d. | Screw propeller | wears | c. | Check | the | supply |
|  |  |  | out |  |  |  |  |  | voltage |  |  |  |
|  |  |  |  |  |  |  |  | d. | Inspect the degrees of |
|  |  |  |  |  |  |  |  |  | screw propeller |  |
|  |  | a. | Raw | materials moisture | a. | Dry raw materials |  |
|  |  |  | is higher than 8-12% | b. | Re-install the heating |
|  |  | b. | The inner slot of heating |  | cylinder | and | inner |
| 6 | The briquettes cannot be |  | cylinder | and | inner |  | housing |  |  |  |
|  | shaped |  | housing dislocation | c. | Sharpening the screw |
|  |  | c. | The screw propeller’s |  | propeller’s front point |
|  |  |  | angle is smaller than 20’ | d. | Fastening the | motor |
|  |  | d. | The motor belt is loose |  | belt |  |  |  |

- Attention Matters

  - Make sure all bolts and screws are fastened.

  - Input the oil in all lubrication site, especially in gearbox.

  - Please attention the voltage, ampere and temperature during production.

  - Discharge port is prohibited people standing.

  - Make sure raw materials not mixed stone pieces, metal scraps, or other things which will damages the briquette machine.

  - All supply power and electric elements must be dry and clean.

  - Please turn-off all supply power after the briquette machine stop.