Liquid filling machine

Operating instructions

Note: This filling machine can only fill liquid without any impurities in it, the filter must be installed before filling,otherwise the pump damage is not covered under warranty due to impurities.

\

I. Machine introduction:

This machine adopts full stainless steel material, electromechanical and electronic control box work together, automated quantitative determination of filling,and automatic counting, a new filing equipment. Simple structure, convenient operation, and the size of the discharge nozzle could be switched easily, and the rubber tube could be moved easily for filling. It could meet 50-1000ml and above filling and infinite.( Any adjustment of the filling capacity requirements, it will not be limited by the filling volume,it is a reliable and durable filling equipment.)

Product Description:

This machine uses a self-priming pump, the pump working time and Intermittent time is controlled by microcomputer,the filling volume and filling time is also controlled by it automatically.It can be used to fill drinks, wine, oil, chemical, oil, pharmaceuticals, pesticides and various other liquids. Not suitable for corrosive liquids. The machine is simple in structure, easy to operate. Nozzle can also lengthened, hose is movable in any way, unlimited filling capacity above 100g, It is a reliable and durable filling equipment. A popular device for small businesses as well as small shops and family useing. Extended hose can be customized convenient and practical.

II. Technical Parameters:

1. Working power: AC 220v 180W

2. Time delay range：0.01s～999.9s

3. Counting range:1～59999

4. Operating modes: power-delay data setup

5. Display: Filling time display on the top row, intermittent time display on the middle row, count display on the bottom row

6. Flow Control: Frequency Control

7. Overlook size: 350*300*200 mm

8. Weight: 9kg

9. Flow capacity:maximum 17L per min

10. Filling nozzle diameter: 10mm (also could make customized,8mm,10mm)

11. Machine material: stainless steel

- Power: AC220V 50Hz allow voltage range（75%）Ue；

- Display way: 3 rows LED display,top row filling time,middle row wait time,bottom count value;

- Filling time: 0.01s～999.9s;

- Maximum count value: 99999times

III. operating instructions

1.Install the machine refer to the above picture；

2. functions：

A ：【filling time】：adjust the pump working time；control the filling range；

B：【waiting time】：it’s the time gap between the first filling and the second；it’s only used for the filler is on Auto set；

C：【counter】：it will counter how many times it has filled；

D：【filling speed】：adjust the filling speed；

E：【setting】：press this button when the filler is on；then the filler will fill；fill your bottles until it is full/or to the volume you need；then press this button again so that the filler will remember the filling range；the filling range is settled；

F：【manual】：switch to manual model and press the button “fixed point” and it will fill as long as you press the button；               G：【auto】：switch to auto model

process：press the red power button on；put your bottle under the filling nozzle；press【setting】to start filling；fill your bottle until the volume you need；press again the【setting】 button；the filler will remember this filling range；then choose the【auto】or【manual】model to start working.