G Type Mower

| G type mower parameter |
| --- |
| Supporting Machine | WM1100 with six gear |
| Dimension (mm) | 880×730×620 |
| N.W/ G.w (kg) | 30 |
| Working Width(mm) | 880 |
| Stub height(mm) | 40mm≤h≤80mm |
| Gear | None |
| Max rotate speed（rpm） | 2600 |
| Clutch | Controlled by WM1100 |
| Applicable range | Mainly for higher plants such as weeds and reeds |

Installation guide

Step one：Install the horizonal and vertical pipe unit

Step two：Install the left&right supporting pipe

Step three：Install the protecting block

Step Four：Connecting the tiller

Caution：

Sub-shift Lever must be in Low gear(L),when the tiller connecting the mower.

# Text boxes

G Type mower explosive view

Right supporting pipe

Horizonal pipe unit

Protecting block

Left supporting pipe

Supporting frame

Cutter assy

M8*20 bolt

#8 washer

#8 gasket

#8 gasket

M8 Bolt

#8 washer

M8*20 bolt

Left supporting pipe

#8 gasket

M8*40 Bolt

#8 washer

Right supporting pipe

M8 Bolt

#8 washer

#8 gasket

Protecting block

M8*30 Bolt

Tiller

#10 washer

M10 bolt

G type mower