目录

一、	适用范围和主要技术参数  
Scope of Use and The Main Specifications	- 1 -

二、	犁的构造及其各部分的作用
Structure of The Plough and The Roles of Each Part	- 1 -

三、	犁的装配Assembling of The Plough	- 2 -

四、	使用和调整Operation and Adjustment	- 3 -

五、	注意事项 Caution	- 5 -

六、	修理： REPAIRING	- 5 -

七、	存放Storing	- 5 -

# 适用范围和主要技术参数  Scope of Use and The Main Specifications

20系列铧式犁为全悬挂式，与标定功率为8.8～33KW拖拉机配套作业。适用于壤土、沙壤土地区熟地旱田耕作。

该系列犁具有结构简单、耕作适应范围广、作业质量好、地表平整、碎土覆盖性能好、墒沟小等特点。

Series of 20 is a mounted bottom plow, designed to match with rated power 8.8KW to 33KW wheel tractor and is suitable for loam，or sandy loam soil in the cultivated area.

This implement is compact in construction, and wide range in application.

It produces the best wort, leaving alevel surface and a narrow furrow, with a good pulverization and mulching. The maximum plowing depth is 25cm.

主要技术参数见表一：

Main specifications see table 1:

| 型号Model 项目Item | 1L-220 | 1L-320 | 1L-420 | 1L-520 |
| --- | --- | --- | --- | --- |
| 犁体个数（个） Nos. of the plough body | 2 | 3 | 4 | 5 |
| 幅宽cm Width | 单犁体幅宽(CM) Furrow width | 20 |
|  | 总幅宽(CM) Total working width | 40 | 60 | 80 | 100 |
| 耕深cm Depth | 20-25 |
| 外形尺寸 Overall dimension (L×W×H) cm | 124*70*96 | 180*82*104 | 240*94*104 | 300*106*104 |
| 运输地隙 Transport clearence | 不小于37cm On les than 37cm |
| 质量kg Weight | 64 | 100 | 130 | 170 |
| 生产率（亩/时） Output (ha/h) | 2.1-2.9 | 2.1-2.9 | 5-6.6 | 7.5 |

# 犁的构造及其各部分的作用Structure of The Plough and The Roles of Each Part

20系列铧式犁由犁架、限深轮、犁体、前犁体部分、后犁体部分组成。（见图一）

The plough consists of frame, depth limit wheel, front plough body assembly and rear plough body assembly. See (Fig. 1)

图一	犁的构造. Fig  Structure of Plough

1、犁架部分	. frame assembly

2、限深轮部分 depth limit assembly

3、前犁体部分 front plough body assembly

4、后犁体部分 rear plough body assembly

犁架由梁架焊合、斜撑杆焊合、前撑杆组成，用来固定各个工作部件，并通过三挂接点与拖拉机连接。

Frame assembly consists of frame welding, deviate support rod welding and front support rod for fixing all the working parts and connect to the tractors by three points.

犁体是犁的主要工作部件，起切土、碎土、翻土、和覆盖杂草的作用。犁体分前犁体和后犁体，其区别是后犁体的犁侧板比前犁体的稍宽、稍长并在尾部装一个犁后踵。每个犁只有一个后犁体。

Plough body is the main working parts of the plough for cutting. Crushing and turning over the soil and cover the grasses and weeds. There is front plough body and rear plough body and the difference between them is the side board of the rear body is wider and longer than the front one, and there is a plough heel assembled behind the rear body. There is only one rear body for each plough.

限深轮用来调节和控制耕深并在存放时起支撑作用，采用力调节或位调节的拖拉机可以不用限深轮。

Depth limit wheel is used for adjust and control the working depth and also support the plough during storage. If the tractors adopt power adjustment or position adjustment, the depth limit wheel can not be used.

# 犁的装配Assembling of The Plough

20系列犁的安装位置及尺寸见表二、图二。

The position and the dimension of 20 series plough’s assembly see table 2 and fig. 2

表二 犁的安装尺寸Table2    Assembling dimension of the plough

单位 unit：mm

| 产品型号Model 安装尺寸 Ass. DIM. | 1L-220 | 1L-320 | 1L-420 | 1L-520 |
| --- | --- | --- | --- | --- |
| L1 | 220 | 230 |
| L2 | 570 |
| L3 | 240-270 | 450-500 | 560 |

Place of depth wheel

图二. 20系列犁的安装示意图   Fig. 2  Assembling of 20 series plough

# 使用和调整Operation and Adjustment

  - 犁在使用前的准备：检查犁的成套性和完善程度，检查零部件安装是否正确紧固，并在限深轮的轮轴与轮毂处注入黄油，耕深调节丝杠处加适量机油。

装配好的犁应达到下列要求：

- 两个犁体的犁铧刃口的高度差，相应不得大于10毫米，各犁铧尖不得上翘。

- 相邻两犁体铧尖的横向距离应为200±10毫米，前后距离为560±15毫米。

Before work it is essential to ensure that ail parts and accessories are in good order and check the tension of nuts and bolts generally. Greas the bearings of the depth wheel, and oll the depth adjusting screw.

Properly assembled plow should meet the following requirements:

- The differences in vertical clearance of the share cutting edges bottoms must be less than 10mm and the share point of a bottom must not be higher than the moving.

- The lateral distance of share points between to adjacent bottoms should be 200±10 mm and the fore-and-aft clearance is 560±15 mm.

  - 犁的田间调整：The major adjustment of the plough

- 耕深调整：

犁的耕深调节采用高度调节方法，既通过限深轮进行调节，将外套管上的紧固螺钉松开，再转动丝杆，顺时针转动时耕深增加，反之则减少，调至所需耕深后将紧固螺钉紧固。

- 犁架左右水平调整：

当犁架左低右高时，可伸长拖拉机右吊杆，右低左高时则相反，直至犁架左右水平为止。

- 犁架前后水平（前后犁体耕深）调整：

前深后浅时，伸长拖拉机上拉杆，反之则缩短上拉杆。

- 耕宽调整：

通过改变悬挂调节杆的长度，可以调节第一犁体的耕宽，伸长悬挂轴调节杆时，第一个犁体耕宽增加，缩短时则相反。

The major adjustment as follow:

- Depth

The working depth is controlled by the depth wheel untighten the bolt on the outer square tube. Turn the adjusting screw clock’s to sink the plow and vice versa, when required depth is achieved, tighten the bolt.

- Lateral leveling

The lateral leveling is done by adjusting the length of the right-hand suspension rod of the tractor lengthening this right-hand suspension rod lowers down the right side but tilts up the left side other plow frame and vice.

- Fore-and-aft leveling

Plow is leveled fore-and –aft by adjusting the length of the tractor top hitch link, shortening the link raises the rear of the plow and vice versa.

- Adjusting the width of cut (s.fig.1)

Front furrow width can be adjusted by changing the length of the adjusting rod of the cross shaft. Extension of the adjusting rod increases width of cut of the front furrow and vice versa.

  - 犁的使用：Operation of the plough

- 工作时限位链应放松，以使犁有适量左右摆动，但摆动量不能过大，以防止升犁后犁碰拖拉机轮胎，因此拖拉机下拉杆的限位链不宜过松。

- 犁在工作中，应经常清除各犁体上沾挂的泥土和杂草，否则影响耕地质量并增加阻力。

- 机组在地头转弯，后退及运输时，必须先将犁升起，以防将犁损坏，远程运输升犁后还应锁定。

- 限深轮轴承处每班注黄油一次。调节丝杆处应经常加适量机油。

Operation

- While the plow is in normal operation, both chains connected to the lower linkages must be loose so that the plow is free to swing sideways. But the check chains shed not be too loose to allow the plow striking the tractor wheels, while in transport position.

- When the plow is in work, the plow bottoms must be free from mud and weeds, other wise, poor plowing quality ands increase in draft would occur.

- When banking or turning the tractor at the headlands, or during transport, it is necessary to raise up the plow form the ground to avoid being damaged. For long distance transport the plow must be raised and locked up.

- Grease the bearings of the depth wheel once a shift. Oil the depth-adjusting screw frequently.

# 注意事项 Caution

  - 犁在工作、运输、回转时，应注意行人和障碍物。

During operation, transportation and reversing, the driver must be carefull for the persons or obstacles nearby.

  - 严禁在犁升起后又不加支撑保险的情况下，在犁下方进行修理和保养。

Repairing or mintaince under the plough during it is lift up without any other surpport is prohibited.

  - 工作时犁上严禁站人。

Anyone is forbiden to stand on the plough during operation.

# 修理： REPAIRING

犁铧磨钝后应及时进行修理，否则影响耕地质量和过分的消耗动力。

- 犁铧刃部磨损不严重时，用磨刀石把犁尖磨利。

- 犁铧刃部磨损严重时，需要进行锻打延展（犁铧背部加厚部分供修理之用）：锻打后要进行刃磨和热处理。

When the share is worn out, it must be sharpened or replaced with a one other wise, it will affect proper plowing and increase the resistance.

- If the share has not worn much, grind it with grindstone from the top side.

- When the share has worn much, it is necessary to have it forged to shape, followed by grinding and a heat treatment.

# 存放Storing

每季工作完毕后，将泥草清理干净，然后对犁进行全面检查，做必要的修理和调整，各润滑处加注黄油和机油，将其存放于干燥的室内或棚里，不可露天存放。

After each working season, clean the soil and the grasses on the plough completely, examine the plough 100%, do necessary repairing and maintained, apply lubricant and machine oil and stored inside dry house or under shade. Open air storage is not allowed.