M300 Root vegetable washer

Instruction Manual

Contents

M300 Root vegetable washer

Ⅰ. Parameters and Functions

Ⅱ. Components Instruction

Ⅲ. Handling Instruction

Ⅳ. Maintenance Instruction

Ⅰ. Parameters and Functions

Name：Root vegetable washer                Material：stainless steel

Type：M300                                         Size: 1550*780*800mm

Power: 1.5 KW                                 Voltage: 220V

Output: 1-1.2ton/h                                Weight: 80kg

Length of brush roller：800mm

Number of brush roller: 6

Features: According to brush's hardness, customize cleaner or peeler. Waste collection plate installable, avoiding waste water polluting the floor.

Details: Mainly consists of motor, speed changer and brush rollers. Absorbing root tuber crops processing machine's characters home and abroad. Brush friction principle. Suitable for circle shape and oval vegetables‘ cleaning and peeling, such as ginger, carrot, taro, potato, sweet potato. Beautiful shape, convenient handling, large capacity, high efficiency, small energy consumption, continuous cleaning, easy handling. Cleaning rods are made of nylon strings, peeling rods are hardening materials, all durable, abrasion-proof. Rotating discharging, hygeian

Ⅱ. Components Instruction

The components’ instruction is as follows:

Ⅲ. Handling Instruction

- Firstly, connect with the water pipe and fix it.

- Connect with the power source and start up the machine, turn on the water pipe switch, letting the machine working without any materials for about 20 seconds to make sure whether all of the brush rollers run or not and to adjust the water flow.

3., the fruit poured into the cleaning tank, generally peeling 3-5 minutes (depending on the amount of processing depending on);

4. open the discharge gate and let the disposal come out.

5. after the work is finished, open the filter screen and clean the waste collection tray

    - After finish washing, pull out the waste collection plate to clean.

      - Instruction for brush rollers’ exchanging:

1. open the outlet screw.

2.Pictures after disassembly

2. open the outlet gate.

3. open the movable door of the electric box and remove the chainthem apart.)

4.Draw out the axle center

5. Demount the brush rollers according to the arrowhead’s direction one by one and then clean or exchange them.

Ⅳ. Maintenance Instruction and Attention

- Every time after finish washing, users should do the cleaning job. Users can wash the washing tank with water while the brush rollers are rolling without other materials. But the motor part, it is forbidden to wash. And the water collection plate at the bottom should be clean in time.

- This machine is suitable for root vegetables washing. Users should pay attention to the washing time. When the washing time is too long, the vegetables’ skins will be easy to damage.

- User had better apply the lubricated grease to the bearings on the two sides of brush rollers every half year.

# Text boxes

Brush roller

Waste collection plate

Discharge valve

Switch

Discharge hole

Waterpipe joint

Motor

After removing the screws, pull out the axle center

The ends of the stick are lubricated regularly