GASOLINE JACK HAMMER

INSTRUCTION MANUAL

User Manual

Welcome to choose our JH95A gasoline jack hammer. This gasoline jack hammer is the lightest weight in the world, lowest emission of small construction machinery. It can crush, tamp, and compact with multinational hand-held tools. And also it can easy to rotate. It surpasses conventional design and brings significant and economic benefits to the user. It has energy saving, and the advantages of easy to use. Reasonable maintenance measures can bring this product work efficiency, longer life to the maximum.

For your safety, please follow the instructions on the safe operation of the rules of operation and technical maintenance, or will cause harm to your personal safety or damage the machine.

Contents

I       Name of Major Part -----------------------------------------------------------------------(2)

II      Instruction of Safe Operation -------------------------------------------------------------(2)

III     Main Use and Feature ----------------------------------------------------------------------(4)

IV     Preparatory Work before Use -------------------------------------------------------------(4)

V      Start -----------------------------------------------------------------------------------------(5)

VI     Run ------------------------------------------------------------------------------------------(5)

VII    Stop Machine -------------------------------------------------------------------------------(5)

VIII   Technical Maintenance --------------------------------------------------------------------(5)

IX    Failure Analysis and Troubleshooting -----------------------------------------------------(8)

X     Product Key Data ----------------------------------------------------------------------------(9)

XI    Maintenance cycle -------------------------------------------------------------------------(10)

XII   Part List of JH95A Gasoline Jack Hammer -------------------------------------------(11)

XIII  Packing List of JH95A Gasoline Jack Hammer------------------------------------------(13)

I    Name of major part

| No. | Parts Name | No. | Parts Name | No. | Parts Name |
| --- | --- | --- | --- | --- | --- |
| 1 | Starter | 2 | Air Filter | 3 | Tank Cap |
| 4 | Fuel Tank | 5 | Fuel Standard | 6 | Gearbox Standard |
| 7 | Gearbox | 8 | Cylinder Block | 9 | Drill Seat |
| 10 | Drill rod | 11 | Drill | 12 | Muffler |
| 13 | Protect Cover | 14 | Handle Bar | 15 | Spark Plug |
| 16 | Oiler Cover | 17 | Flame-out Button | 18 | Gearbox Cover |
| 19 | Ventilation Door |  |  |  |  |

II   Instruction of safe operation

- The operator should wear slip-resistant safety shoes and appropriate clothing. Wear goggles and helmet, wear earplugs for a long time operation.

- Balance the body when you operate the machine. Operating the machine in a right position as shown in Figure 1 instead of Figure 2

- No smoking, eating or chatting when you operate the machine.

- One-handed performance is not allowed after the machine is started.

- When you lift machine, the first control you need dial to reach the minimum scale, let the machine to slow down.

- Non-staff should keep away from the work area to avoid injury. The process of using machine may lead to gravel flying to non-staff.

- Select medium-speed gasoline hammer to run for the best.

- In the use of operation, the operator is not equal to the greater pressure crushing, tamping, compacting faster, try to use the weight of the machine itself, the force should be reasonable in order to achieve high efficiency and easy operation results.

- Gasoline hammer for crushing, tamping, compacting work, the work can not be used to pry the stone.

- Maintain the handles dry and clean, no oil or fuel mixture.

- Stop the operation midway; you must turn off the engine.

- Please check normal fastening screws of the connector before using in each time. If loose, you must tighten the screws to use.

- Pure gasoline (without two-stroke engine oil) for fuel is prohibited, match according to the proportion recommended in Chapter 4.2.

- Gasoline is highly flammable, so to refuel in a well-ventilated environment. When you add fuel, please stop gasoline engine.

- Do not add fuel too full; do not leave the fuel filler in neck part of machine. If overflow or spilled fuel .wait the fuel all volatilize, then you can start machine.

- After refueling, tighten the fuel cap. Please check frequently whether the fuel tank is damaged to leak, if found damaged replace immediately.

- Reserve fuel in storage areas. Remove all the root causes of fire or cause sparks.

- In closed areas, such as tunnels, trenches and deep groove in the work environment when using gasoline hammer to ensure sufficient fresh air, exhaust gas containing carbon monoxide dangers, should bring electric fan for air flow.

- Quickly acceleration or sudden braking is not allowed, so as not to damage the machine.

- Avoid the impact of fragmentation work against the machine in the context of high speed operation.

- Transfer site long-distance transport, should be emptying the tank.

- Substandard maintenance staff should not dismantle the gasoline hammer to avoid structural damage to the parts, and further resulting in shortened life of gasoline hammer or accidents.

Figure 1  Right                              Figure 2  Wrong

III   Main use and feature

Use

1 It can be used in crushing of building construction and road building project.

2 Break cornerstone for the railway road and tamp sleepers work.

3 Ditching works of embedded telecommunications cables

4 Ice-breaking works in cold water and frozen region with digging shovel.

Features

1 It is the world’s lightest weight, lowest emission engine type hand-held gasoline hammer.

2 A perfect body and “V” linear operation, minimizing the hands of vibration, has significant control of convenience and comfortable, the operator can shovel digging a 360 degree rotation.

3 It can regulate the number of impact energy and impact, apply for a variety of materials suitable for construction.

4 Applications: Our machine is applicable to a variety of conditions, such as crashing project in road-building, electric power, telecom, and cable, ditch.

Advantage: If you use our machine, then you can ignore the trouble of the heavy equipment like diesel engine, air compressor, trucking-lorry, which will not limited by the pipe line, electric line, cable no matter how high and how far, we can work in kinds of environment.

IV   Prepared work before using

Installation

1. Take out the drill rod (head) and lubricate the drill.

2. Parallel the gap between the drill rod and the stop rod; pull the stop rod according to the direction of arrow, and lock or loosen the drill rod after rotating for 180° (see Figure 3).

3. Pull out the drill rod, insert the drill into the drill seat then make sure locked up the drill.

Figure 3                                      Figure 4

Fuel

The general gasoline and the two-stroke oil mix.

Recommended mixing ratio

| Conditions | gasoline :engine oil |
| --- | --- |
| Work within 20 hours | 20:1 |
| Work after 20 hours | 25:1 |

- Prohibit the use of pure gasoline (no refueling two-stroke engine oil )for fuel

- Well-ventilated place to add fuel

- Do not add too full fuel in the fuel tank. Do not leave fuel in the neck. If any fuel spill, please completely remove or evaporate before starting the gasoline engine

- After refueling, tighten the fuel tank cap.

V   Start

1. Before first starting of the new machine, repeat press the transparent fuel bubble (See Figure 4) to fully fill the Carburetor with fuel. (When the refrigerator starts, turn off the ventilation door. When the gasoline engine starts, open the ventilation door and turn on the spanner)

2. Hold the operation handle with one of your hands and quickly pull the pulling handle for about 50cm with the other hand. Do not let the pulling handle go back freely in your repeat pulling, but hold it and put it down with its resilience to protect the starter.

3. Open the air vent completely when the gasoline engine is started.

Figure 5                                     Figure 6

VI   Run

1. After the gasoline engine starts, it should run at low speed for 2 to 3 minutes to preheat the machine.

2. When the gasoline engine warm enough, according to the required impact energy to pull appropriate regulatory position.

Note: ① the new gasoline hammer use of the first 24 hours, the workload should be in low-speed in order to extent the service life.

②Just start poor lubrication of gasoline, do not accelerate quickly.

3. Select medium-speed gasoline engine run for the best.

4. Do not use the gasoline hammer under the non-breaking with high speed operation.

VII    Stop machine

- Loosen the accelerator switch, and idle running for 1-2 minutes.

- Press the red button to stop. See the position of stop switch in Figure 6

VIII   Technical maintenance

1 Air Filter

Check the air filter regularly. Dust block on the cover of air filter will reduce engine power, causing short life of the cylinder. If the filter is very dirty, bur a mild detergent with warm water, wring dry, after cleaning the filter should drop a few of oil on the dry and then install the air filter. Filter should be replaced if damaged, particularly if in the environment of much dust should be shorted maintenance cycle.

2 Fuel filter

If the fuel filter is clogged, the machine will be slowed down and impact energy will be weakened. Method: ① Open the tank cap (See Figure 7) with metal hook (See Figure 8,9), take the fuel filter cleaning from the tank  ②When cleaning the fuel filter, clean the fuel tank at same time.

3 Carburetor

Fuel tank and carburetor will generally have left residual fuel. After a certain period, the residual fuel will come into rubbish. And the rubbish will plug the fuel line, causing the engine does not work. Therefore, when the machine is not used more than one week, be sure to completely take the fuel out. Method: processing the carburetor fuel bubble to drain the fuel again.

4 Spark plug

To ensure normal operation of the engine, spark plug gap to be moderate, with a wire brush to remove sediment. Reasonable spark plug gap 0.5-0.7 mm. See Figure 10

Figure 10

5 Muffler

Regular maintenance muffler, use a screwdriver to remove rubbish on the body or the rubbish on the coke muffler exhaust.

6 Gear box grease

Open the gear box cover, add grease to drive gear on a regular basis to ensure full gear lubrication.

7 The cylinder cooling fin

Regularly to remove dust, to ensure the cylinder cooling, this gasoline hammer is air-cooler type, if the cylinder dust accumulates on the cooling fin will directly affect the cooling effect. Dust is easy to make the engine break down.

8 Refueling the impact air cylinder lubricating grease

After the machine has run for cumulatively 50 hours, 50g of special grease shall be refueled to the impact air cylinder, see Figure 11, 12, 13 and 14.

Figure 11                                 Figure 12

Figure 13                                  Figure 14

IX Failure analysis and troubleshooting methods

Problems analysis and solving

Example1: difficulties in starting engine in cooling state.

| Whether the spark plug is moisture. | →Dry the igniter plug |
| --- | --- |

↓

| Whether the spark plug produces electric spark | →replace the igniter plug |
| --- | --- |

↓

| Too much fuel absorbed | →lessen the fuel supply |
| --- | --- |

Example 2: Difficulties in restarting after a sudden stop

| Whether fuel runs out or the Carburetor is blocked | →Refill fuel tank or clean the carburetor |
| --- | --- |

↓

| Whether the fuel filter is blocked | →clean the fuel filter |
| --- | --- |

↓

| Too much carbon deposit in igniter plug | → Remove carbon deposit |
| --- | --- |

Example 3: Reluctance in speeding and weakness in power

| Carbon deposit cover the entrance of the cylinder or silencer | → Remove carbon deposit |
| --- | --- |

↓

| Whether the fuel tube and the air vent on the fuel Tank cover is blocked | →Clean |
| --- | --- |

↓

| Blockage in air filter | → Clean the filter |
| --- | --- |

Example 4: abnormal sound

| Carbon deposit found in combustion chamber | → Remove carbon deposit |
| --- | --- |

↓

| Serious abrasion in active components | → Replace |
| --- | --- |

Example 5: The machine is working normally, but the efficiency of cracking is very low

| The head of the chisel is attrited badly | →replaced or renew |
| --- | --- |

Please contact with Sales Agency of the Crusher if your machine needs further mending.

X  Product key data

| Engine type | Single cylinder, air cooling, 2 stroke, X stroke of cylinder diameter; 44X34mm |
| --- | --- |
| Model number | JH95A |
| L×W×H(mm) | 690×370×270 |
| Fuel | mixing fuel (gasoline 25, two-stroke engine oil=25: 1) |
| Fuel tank capacity | 1.3L |
| Weight | 20.50Kg |
| Emission | 52cc |
| Max power and speed | 1700W/9000r/min |
| Max torque and speed | 2.5N.m/5000r/min |
| Consumption rate | ≤0.6L/h |
| Impact frequency | 700~1350BPM |
| Impact energy | 20~55J |
| Carburetor type | H119-6A-00-210 |
| Spark plug type | BM6A |
| Starter system | Hand pull start |

XI Maintenance Cycle

| The following Data are given common use of the product. Suppose it is in worse working condition, such as thick dust in the air or much longer work hours for Crusher, the maintenance cycle should be shortened correspondingly. | Before woke | After work or every day | After Filling fuel | Every Week | Every Month | Broken Down | If necessary |
| --- | --- | --- | --- | --- | --- | --- | --- |
| The whole machine | outlook check (state, stabilities of screws) | √ |  | √ |  |  |  |  |
|  | Cleaning |  | √ |  |  |  |  |  |
| Control handle/stop button | function check | √ |  | √ |  |  |  |  |
| Air Filter | Clean |  |  |  | √ |  |  | √ |
|  | Replace |  |  |  |  |  | √ |  |
| Fuel Filter | Check |  |  |  |  | √ |  |  |
|  | Replace |  |  |  |  |  | √ |  |
| Petrol Tank/Petrol Tank cover | Clean |  | √ | √ |  |  |  |  |
|  | Check | √ |  | √ |  |  |  |  |
|  | Tighten |  |  |  |  |  |  | √ |
| Gear Box/Hammer Box | Clean |  |  |  |  | √ |  |  |
|  | Add fuel |  |  |  |  |  |  | √ |
| Lubricating fuel Tank | Check | √ |  |  |  |  |  |  |
|  | Clean |  |  |  |  | √ |  |  |
|  | Fill fuel |  |  |  |  |  |  | √ |
| Chisel | Check Sharpness | √ |  |  |  |  |  |  |
|  | Sharpen or Forge |  |  |  |  |  |  | √ |
|  | Replace |  |  |  |  |  | √ |  |
| Silencer | Check |  |  |  |  | √ |  |  |
|  | Remove carbon deposit |  |  |  |  |  |  | √ |
| Cylinder Cooling Fin | Check |  |  |  |  | √ |  |  |
|  | Clean |  |  |  |  |  |  | √ |
| lignite Plug | Check/Adjust Customize the distance between electrodes |  |  |  |  | √ |  |  |
|  | Replace |  |  |  |  |  |  | √ |
| Screw and Nut | Check | √ |  | √ |  |  |  |  |
|  | Tighten |  |  |  |  |  |  | √ |

XII    Part list of TT95A GASOLINE JACK HAMMER

| No. | Part Name | QTY |  | No. | Part Name | QTY |  | No. | Part Name | QTY |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Start Handle | 1 |  | 41 | Straight pin | 2 |  | 81 | Stop Button | 1 |
| 2 | Screw M5x20 | 13 |  | 42 | Fan Cover | 1 |  | 82 | Washer 6 | 1 |
| 3 | Elastic Washer 5 | 21 |  | 43 | Washer 6 | 6 |  | 83 | Screw M6x20 | 10 |
| 4 | Washer 5 | 23 |  | 44 | Elastic Washer 6 | 4 |  | 84 | Bearing 6203 | 2 |
| 5 | Cap Assembly | 1 |  | 45 | Screw M6x25 | 4 |  | 85 | Pinion | 1 |
| 6 | Fuel Return Pipe | 1 |  | 46 | Screw M5x15 | 1 |  | 86 | Gear shaft | 1 |
| 7 | Plug | 1 |  | 47 | Screw M6x60 | 2 |  | 87 | Circlip for Hole 40 | 1 |
| 8 | Fuel Pipe | 1 |  | 48 | Muffler | 1 |  | 88 | Circlip for Axis 17 | 1 |
| 9 | Filter | 1 |  | 49 | Gasket | 1 |  | 89 | Intermediate gear | 1 |
| 10 | Screw st4.8x13 | 1 |  | 50 | Ignition Coil Comp | 1 |  | 90 | Bearing 6204 | 1 |
| 11 | Cover | 1 |  | 51 | Cord Comp | 1 |  | 91 | Bearing Plate | 1 |
| 12 | fuel immersion lens | 1 |  | 52 | Outer cover buckle | 1 |  | 92 | Screw M5x10 | 4 |
| 13 | Fuel Tank | 1 |  | 53 | Pan head screw | 1 |  | 93 | Big gear | 1 |
| 14 | Recoil Spring | 1 |  | 54 | Outer cover | 1 |  | 94 | Bearing 6202 | 1 |
| 15 | Rope | 1 |  | 55 | Spark Cap | 1 |  | 95 | Inflating Plate | 1 |
| 16 | Start Rope Reel | 1 |  | 56 | Cylinder | 1 |  | 96 | Bearing 6205 | 1 |
| 17 | Start Spring | 1 |  | 57 | Gasket | 1 |  | 97 | Bent axle | 1 |
| 18 | Start Claw Assembly | 2 |  | 58 | Gasket | 1 |  | 98 | Needle Bearing | 1 |
| 19 | Nut M8 | 1 |  | 59 | Admitting Pipe | 1 |  | 99 | Bent axle check ring | 1 |
| 20 | Start Reel | 1 |  | 60 | Screw M5x25 | 2 |  | 100 | Bolt M8x20 | 1 |
| 21 | Gasket | 1 |  | 61 | Carburetor Gasket | 1 |  | 101 | Plug | 1 |
| 22 | Piston | 2 |  | 62 | Carburetor | 1 |  | 102 | Fuel box cover | 1 |
| 23 | Circlip | 1 |  | 63 | Screw M5x50 | 2 |  | 103 | Fuel box seal ring | 1 |
| 24 | Piston Pin | 2 |  | 64 | Filter Net | 1 |  | 104 | Gear Box | 1 |
| 25 | Piston Ring | 1 |  | 65 | Air Filter Seat | 1 |  | 105 | Real Gasket | 1 |
| 26 | Crank Shaft | 1 |  | 66 | Air Filter Cover | 1 |  | 106 | Connecting Rod | 1 |
| 27 | Needle bearing | 1 |  | 67 | Screw M5x16 | 6 |  | 107 | Igniter Plug | 1 |
| 28 | Right Crank Case | 1 |  | 68 | Washer 5 | 1 |  | 108 | Lip-shaped ring | 1 |
| 29 | Gasket | 1 |  | 69 | Throttling Cock Cover | 1 |  | 109 | O-shaped ring | 1 |
| 30 | Fuel-seal 12x22x7 | 1 |  | 70 | Throttling Cock Spanner | 1 |  | 110 | Impact cylinder | 1 |
| 31 | Bearing 6202 | 2 |  | 71 | Cable accelerator | 1 |  | 111 | Front placket | 1 |
| 32 | Woodruff key 3x5x13 | 1 |  | 72 | Throttling Cock Spring | 1 |  | 112 | Washer 8 | 10 |
| 33 | Fuel-seal 15x30x7 | 1 |  | 73 | Throttling Cock Base | 1 |  | 113 | Bolt M8x35 | 4 |
| 34 | Straight pin 5x10 | 2 |  | 74 | Nut M5 | 1 |  | 114 | Iron hoop | 2 |
| 35 | Left Crank Case | 1 |  | 75 | Bolt M8x30 | 3 |  | 115 | Small Damping Ring | 1 |
| 36 | Screw M5x35 | 4 |  | 76 | Washer 8 | 4 |  | 116 | Split Ring | 1 |
| 37 | Magneto Rotor Comp | 1 |  | 77 | Nut M8 | 4 |  | 117 | Piston Pin | 1 |
| 38 | Shoe Block Spring | 1 |  | 78 | Handle Spring | 4 |  | 118 | Split Ring Rubber Circle | 1 |
| 39 | Shoe Block | 1 |  | 79 | Handle | 2 |  | 119 | Handspike cover | 1 |
| 40 | Axial screw | 2 |  | 80 | Handle Rack | 1 |  | 120 | O-shaped ring | 1 |
| No. | Part Name | QTY |
| 121 | Big Damping Ring | 1 |
| 122 | Front Gasket | 1 |
| 123 | Iron head | 1 |
| 124 | Stop rod | 1 |
| 125 | Screw M8x30 | 6 |
| 126 | Stop rod spring | 1 |
| 127 | Washer | 1 |
| 128 | Soft Washer | 2 |
| 129 | Lock sleeve | 1 |
| 130 | Straight pin 4x18 | 1 |
| 131 | Gear box cover seal ring | 1 |
| 132 | Gear box cover | 1 |
| 133 | Screw M6x16 | 6 |

XIII  Packing list of JH95A product

1.Jack hammer..................................................................................................1

2.Pick........................................................................2 (sharp and flat)

- Matching oiler...........................................................................................1

4. Grease for cylinder (60g)..........................................................................1

5.Manual................................................................................................1

6. Kit (including 1 sparking plug, 1 socket head spanner of 6mm, 1 straight screwdriver, 1 sparking plug handle, 1 socket head spanner of 8mm and 1 Fuel leveler spanner)

# Text boxes

13

12

11

10

9

8

6

5

7

4

3

2

1

Pull out the drill rod. Then turn 180°which is lock or unlock.

Fuel Bubble

Stop Button

ON

OFF

Figure 99

Figure 88

Figure77777